## Slide 1: Construction vehicle access and egress for roadway construction
Access and Egress
PREVENTING RUNOVERS AND BACKOVERS IN ROADWAY CONSTRUCTION
Construction Vehicle
for Roadway Construction
Access and Egress
Notes: This module focuses on how ITCP planning can improve safety at vehicle entry and exit points. It explains how access/egress locations provide transitions between TTC plans and ITC plans.

## Slide 2: ARTBA Disclaimer
This material was produced under the grant SH-24861-SH3 from the Occupational Safety and Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government.
Additional assistance came from contract 212-2009-M-32109 from the National Institute for Occupational Safety and Health.
Contact ARTBA for information about Student Handbooks.
American Road & Transportation Builders Association

## Slide 3: Course goals
Access and Egress
PREVENTING RUNOVERS AND BACKOVERS IN ROADWAY CONSTRUCTION
  Why control of access and egress is so important
At the end of this module, you will know
  Challenges in access and egress
  How the ITCP addresses each challenge
  How FHWA Subpart K impacts access and egress
Access and egress are a critical aspect of a well-planned ITCP.

## Slide 4: Why is access and egress control important
Access and Egress
PREVENTING RUNOVERS AND BACKOVERS IN ROADWAY CONSTRUCTION
Access to / egress from work zones presents significant challenges
Why Is Access and Egress Control Important?
Hazards compound when a roadway
Safety challenges include
  - Motorists following construction vehicles into the work space
  - Acceleration and deceleration of construction vehicles as they exit/enter open traffic lanes
  - Proximity of workers on foot to access and egress locations
  - Carries high traffic volumes
  - Operates at high traffic speeds
Notes: Why is access and egress control important? (Discuss this question.)
The establishment and maintenance of safe access and egress points are key determinants of project safety. In order for roadway construction jobs to maintain safe operations, there must be procedures to allow for safe and efficient passage of work vehicles into and out of the work space and for motorists to travel through the work zone. Effectively addressing safe access and egress at the project level requires planning during the project development phase and implementing traffic control plans throughout the entire project.

## Slide 5: Access and egress challenges
  - Short or Non-existent
Acceleration / Deceleration Lanes
Signing for Merge / Exit Points
  - Signs giving vague information
Access and Egress
PREVENTING RUNOVERS AND BACKOVERS IN ROADWAY CONSTRUCTION
Primary Challenge: Safely and efficiently getting materials and equipment into and/or out of work zone
Access and Egress Challenges
  - Messages left up 24 / 7
Attendant Challenges:
Flagging Operations
  - Best with low traffic, moderate trucks
  - Rules are forgotten
  - Low trucks = intermittent flagging
Night Work
  - Poor sight distance, impaired drivers, others?
Notes: The primary challenge with regards to work zone access and egress is getting materials in and out of the work space. Of necessity, this involves acceleration and deceleration of large, heavy trucks and equipment hauling the materials. These construction vehicles must leave and enter the traffic space, where motorists often drive at high speeds, and transition to the work space, filled with slow moving equipment and workers on foot.

## Slide 6: Access and egress picture
Access and Egress
PREVENTING RUNOVERS AND BACKOVERS IN ROADWAY CONSTRUCTION
ITCPs Coordinate Tasks
SEE WORKBOOK PAGE 5
Delivery access
and egress point.
Moving construction
Equipment.
Parked employee
vehicles.
Workers
on Foot.
Notes: The work area can be complex with delivery trucks entering and exiting the work space near workers on foot and other operating/moving equipment. The ITCP should coordinate these activities so all know what the other is doing and each stays out of the path of the other. In this slide, the employee vehicle and worker on foot would be in direct path of a vehicle entering the work area. A risk analysis would identify the location of the parked vehicle as a hazard; a different parking site should be identified. Employer should train employees on where to and where not to park on site. Employers should also train on particularly hazardous areas like access and egress points.
Workers, operators and drivers inside the workspace should be aware and vigilant when working near access and egress points. Drivers entering the work space likewise need to be very attentive when doing so as this is a high-hazard area for all workers.

## Slide 7: Access and egress challenges can be addressed by an ITCP
QC Truck
Foreman Truck
GW Truck
QC
SI
Enter
Exit
GW
SI
SO
SP
SI Truck
Breakdown Lane 10’
Lane 2 10’
Lane 1 10’
Staging Area
Worker Area
Access and Egress
PREVENTING RUNOVERS AND BACKOVERS IN ROADWAY CONSTRUCTION
Access/egress challenges can be addressed by an ITCP
  - Isolating workers on foot from trucks and equipment
  - Coordinating truck and equipment movements
  - Limiting/controlling vehicle access points
  - Providing guidance to workers on foot, truck drivers, and equipment operators
  - Designating locations for parked vehicles and equipment
  - Raising awareness about vehicle intrusions with workers and operators/drivers

## Slide 8: Challenge number 1
Access and Egress
PREVENTING RUNOVERS AND BACKOVERS IN ROADWAY CONSTRUCTION
Trucks entering the work zone put motorists and those on other side of wall at risk
Challenge #1
ITCP solutions
Train truckers to pay attention to work space dynamics
Instruct workers to stay clear of access and egress points
Instruct employees on proper locations for parking and staging vehicles, away from entry and exit points
Notes: Entering and exiting the work space can require rapid acceleration and deceleration. (Discuss with the class the dynamics of how this situation is impacted if the truck in loaded or empty. Taking the load into consideration, how might that knowledge be used to make the work environment safer?
Activities that occur under the direction of construction contractors include maintaining a clear/open area around access/egress points where equipment or vehicles should not be parked. Contractors are also responsible for educating on-site employees about areas near access/egress points that are prone to heavy truck traffic. Workers should avoid crossing open traffic lanes, particularly those on high-speed roadways.

## Slide 9: Challenge number 2
Access and Egress
PREVENTING RUNOVERS AND BACKOVERS IN ROADWAY CONSTRUCTION
Trucks queued inside work zone create obstacles for workers and operators
Challenge #2
ITCP solution
If queues threaten to block access and egress locations, queues should be redirected, or different access and egress spots should be opened and identified for drivers to use
Notes: When truck queues form near exit and entry points they create hazards for other vehicles attempting to enter (with little deceleration space) and exit (with little acceleration space). If queues threaten to block these spots, queues should be redirect, or different access and egress spots should be identified for drivers to use.
If queues threaten to block access and egress locations, queues should be redirected, or different access and egress spots should be opened and identified for drivers to use.

## Slide 10: Challenge number 3
Access and Egress
PREVENTING RUNOVERS AND BACKOVERS IN ROADWAY CONSTRUCTION
Trucks do not have enough space to slow down when entering or to match traffic speeds when exiting
Challenge #3
ITCP solution
Use shoulder areas or closed lanes to create ramps for safe acceleration/deceleration zones
Notes: Speed differential between traffic lanes and work space is a challenge for truck drivers, and can create significant hazards for both workers and motorists.
In addition to creating special ramps or other lanes, all access and egress areas should be kept clear of debris, signage, parked vehicles, etc.

## Slide 11: Challenge number 4
- Trucks entering/exiting
  - Stopped traffic warning
  - Maintain TTCDs in good condition
Access and Egress
PREVENTING RUNOVERS AND BACKOVERS IN ROADWAY CONSTRUCTION
Motorists follow construction trucks into the work area
Challenge #4
ITCP solutions
Traditional warnings - Slow speed advisory
  Vehicle-activated warning signs - Replace signs on vehicles - Real-time information
  - Dynamic Lane Merge
  - Travel time/delay
  - Excessive speed warning
  - Traffic surveillance
Notes: Because construction trucks tend to be very large, motorists directly behind them cannot see the road ahead or some traffic signs. Because of this lack of sight distance, they may not realize the truck is leaving the traffic space and entering the work space and follow it. Signs mounted on the truck or additional work zone signs or signals can provide additional guidance to drivers.
Warning signs alert motorists to be aware of slow moving construction vehicles. If motorists make room for trucks to enter and exit travel lanes, safety is improved inside the work space as construction drivers may not need to change their speeds so abruptly.
Motorists are likely to pay more attention to information that is correct, up-to-date and relevant. Vehicle activated signs that provide warning messages only when trucks are entering or exiting the work space are more likely to be heeded by motorists than static signs that may not be relevant to the immediate situation. Use of these signs improves access and egress safety by informing motorists to slow down and to expect and encounter with a slow-moving truck or other vehicle.

## Slide 12: Challenge number 5
Access and Egress
PREVENTING RUNOVERS AND BACKOVERS IN ROADWAY CONSTRUCTION
Crew, operators, inspectors, subcontractors, others may not be up-to-date on access/egress locations as work progresses
Challenge #5
ITCP solutions
Hold pre‐shift meeting with all involved
Inform everyone on daily activities and changes
Notes: Roadway construction involves moving operations. As the work progresses, so moves the work site. With continual changing conditions, access and egress points may change.
The best way to keep all members of the construction team up-to-date is to hold pre-shift meetings where the day’s activities are discussed and those involved can receive updates.

## Slide 13: Challenge number 6
Access and Egress
PREVENTING RUNOVERS AND BACKOVERS IN ROADWAY CONSTRUCTION
Motorists may breach barriers and strike workers near access and egress points
Challenge #6
ITCP solutions
When openings are not in use they should be evaluated to see if it is necessary to close them
Watch for vehicles that do not belong in or near the work area
Check for problems such as blunt ends on barriers
Notes: Access and egress points require gaps in barriers and traffic delineation. These gaps can allow traffic to enter the work space unimpeded and therefore create increased exposures to workers.
Temporary traffic control devices, particularly end treatments, should be checked regularly to ensure they are in good operating condition. Part of the ITCP is to evaluate end treatments when access/egress points are opened and closed.

## Slide 14: Challenge number 7
Access and Egress
PREVENTING RUNOVERS AND BACKOVERS IN ROADWAY CONSTRUCTION
Emergency responders need access when incidents occur within the work zone
Challenge #7
ITCP solutions
The Temporary Traffic Control Plan (TTCP) and the Internal Traffic Control Plan (ITCP) should function together to allow access for emergency responders
Evaluate each job – when appropriate, local police should be kept up to date on activities that disrupt traffic and have the potential for workers to be harmed
Law enforcement and emergency responders need to know what is happening on your jobsite
Notes: Each place of work should have a site-specific plan in place to deal with an emergency. There should always be someone onsite that knows who to call in the event of an emergency and can provide instructions on what actions to take.
The TTCP and ITCP need to include provisions for providing access to emergency responders in the event there is an incident within the work space. Communicating current conditions about traffic control within the workspace to first responders is an important consideration in the ITCP. This will change with every job. Even in non-emergency situations, it is helpful to keep local law enforcement officials informed about site conditions and operations should their assistance be required.

## Slide 15: Federal regulations
Requires States to consider road user and worker safety by addressing:
Access and Egress
PREVENTING RUNOVERS AND BACKOVERS IN ROADWAY CONSTRUCTION
Traffic Control Devices Rule - 23 CFR 630 (Subpart K) Effective December 04, 2008
Federal Regulations
Use of positive protection devices to prevent intrusions
Exposure control measures
Other traffic control measures to minimize crashes
Safe entry/exit of work vehicles/ equipment from the travel lanes
Notes: The Federal Highway Administration included language in its recent regulation, known as Subpart K, requiring agencies and contractors to give more attention to the hazards posted by roadway construction access and egress points.

## Slide 16: Discussion and questions
Access and Egress
PREVENTING RUNOVERS AND BACKOVERS IN ROADWAY CONSTRUCTION
Discussion and Questions