## Slide 1: OSHA NOTICE & DISCLAIMER
“This material was produced under grant SH20866SH0 from the Occupational Safety and Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government”

## Slide 2: EQUIPMENT SAFETY FOR LOGGING (Module #7)
MAJOR MOBILE EQUIPMENT INCLUDES:
FELLER-BUNCHER – Harvests trees!
SKIDDER – Grapple – Drags them to the landing…
De-LIMBER – Strips off branches and cuts to length…
Dangle-HEAD – Another way to remove branches and cut to length…
Loader – Gets the logs on the truck at the landing…

## Slide 3: ABOUT the FELLER - BUNCHER
A Dangerous & Powerful machine!
This equipment uses a spinning disc to slice through trees.
Feller bunchers are mounted on Caterpillar tractors.
The maximum cab angle on a hill side. Slope is 55°.
Watch the following videos to see what this machine can do.

## Slide 4: SAFETY FACTS ABOUT THE FELLER-BUNCHER WHAT YOU NEED TO KNOW 1-stay back 300 feet from this machine 2- this machine throws chips & rocks a long way. 3-the spinning disk operates on inertia.

## Slide 5: Feller -Buncher close up WHAT YOU NEED TO KNOW 1-this large diameter disk slices through trees 2-the disc and its teeth are mounted and secured by bolts

## Slide 6: CHECK THAT DISC IN THE FIELD! WHAT YOU NEED TO KNOW 1-check for wobbling 2-check for loose teeth and bolts

## Slide 7: FELLER-BUNCHER STARTUP WHAT YOU NEED TO KNOW 1-angle boom is drawn close to After startup 2- Cab is leveled for climb uphill 3-Swivels to check for other persons or equipment nearby.

## Slide 8: WHAT THE FELLER-BUNCHER CAN DO WHAT YOU NEED TO KNOW 1-notice how far debris can be thrown 2-look at that spinning disk 3-logs are easily moved around.

## Slide 9: Feller-buncher a little too close WHAT YOU NEED TO KNOW 1-the debris thrown includes soil, rocks, and any metal lying about 2-this is too close for comfort!

## Slide 10: FELLER-BUNCHER SHUT DOWN WHAT YOU NEED TO KNOW 1-Rolls downhill 2-blade contacts ground and throws material 3-blade continues to spin until out of inertia-no immediate shutdown.

## Slide 11: QUICK TEST
Answer this question:
Question: what are some safe operating rules for working around a feller Buncher?
A – stay at least 300 feet away B – wear protective equipment to guard against the impact of ejecting materials
C – the climb angle is a maximum of 55°
D – all the above.

## Slide 12: ABOUT the SKIDDER - GRAPPLE
The skidder grapple’s job is to move logs from harvest down to a landing.
There are two types of skidders.
One type is a skidder grapple mounted on rubber tires.
The other type is a skidder grapple mounted on caterpillar tracks.
Both types of units are operated by a driver who has a limited field of view.
All persons on the ground must make eye contact with the driver.
It is your responsibility to be visible and to stay out of the way.

## Slide 13: SKIDDER OPERATION WHAT YOU NEED TO KNOW 1-the claw is closed and lowered for movement. 2-the driver looks in the direction of travel 3-other equipment is in area.

## Slide 14: SKIDDER OPERATIONS CONTINUED WHAT YOU NEED TO KNOW 1-other equipment operates nearby. 2-operate machines away from trees a distance of 2 times height. 3- watch for debris

## Slide 15: EXPOSURE TO THE SKIDDER OPERATOR WHAT YOU NEED TO KNOW 1-the skidder passes through a cloud of thrown debris 2-imagine what would happen if windows were not present 3-if you were on the ground-you would need a hardhat.

## Slide 16: LOG DRAG WHAT YOU NEED TO KNOW 1-the skidder gathers logs 2-as many logs as possible are dragged down to the landing

## Slide 17: THE CAT TRACK SKIDDER WHAT YOU NEED TO KNOW 1-this unit can pivot in place 2-it may go off balance. If on an unstable surface 3-materials, including logs, can be caught up in the tracks.

## Slide 18: MORE ABOUT THE CAT TRACK SKIDDER WHAT YOU NEED TO KNOW 1-smaller diameter trees can be caught in the Tracks 2- some of these trees can bend and break with explosive force 3-a Jill Poke is the term used to describe a log or Pole under bind that can snap and penetrate the cab glass.

## Slide 19: QUICK TEST
Answer this question:
Question: what are some safe operating rules for working around skidders?
A – stay visible! Wear high visibility garments. B – make eye contact with the equipment operator.
C – stay out of blind spots and as far away as possible.
D – all the above.

## Slide 20: ABOUT The De-LIMBER
The delimber is a device that grabs logs and removes the branches.
The log is grabbed in place and also cut to length.
The unused portion of the logs dropped from height.
Keep your distance from this machine, because it can throw materials in any direction.
The operator has a limited field of view.
He may not be able to see you on the sides or behind the machine.
The chainsaw guy mounted on this device may throw the chain if it becomes unsecured.

## Slide 21: DELIMBER WHAT YOU NEED TO KNOW 1-this equipment is mounted on Tracks 2-the equipment may swivel at any time 3-the most dangerous portion is directly in front as the boom extends and cuts.

## Slide 22: THE DELIMBER IN ACTION WHAT YOU NEED TO KNOW 1-sometimes rocks and metal are embedded in the bark and limbs 2-the tips of the logs will drop off when cut so avoid being underneath or around them.

## Slide 23: MORE DELIMBER ACTION WHAT YOU NEED TO KNOW 1-other equipment in the area. 2-equipment operates close to each other. 3-avoid this area.

## Slide 24: QUICK TEST
Answer this question:
Question: what are some safe operating rules for working around delimbers?
A – stay visible! Wear high visibility garments. B – make eye contact with the equipment operator.
C – stay out of blind spots and as far away as possible.
D – all the above.

## Slide 25: LET’S TAKE A BREAK
Let’s take 5 min. to get a drink of water and do whatever we have to do then we will return and finish……

## Slide 26: The DANGLE-HEAD
The dangle head is often called the harvester head.
It is another type of delimber.
The same types of precautions apply.
Stay in plain view of the equipment operator-if you don’t, you may not be seen because the dangle head is in the way.

## Slide 27: THE DANGLE HEAD OPERATORS JOB WHAT YOU NEED TO KNOW 1-know, what else and Who else is in the area! 2-know where people are located 3-coordinate activity.
Notes: Works close to a loader, watch where personnel on landing are what else & who else in area

## Slide 28: MORE ABOUT THE DANGLE HEAD WHAT YOU NEED TO KNOW 1-this unit operates close to the ground. 2-it weighs several hundred pounds 3-.stay away from it to avoid getting hit.

## Slide 29: QUICK TEST
Answer this question:
Question: what are some safe operating rules for working around dangleheads?
A – stay visible! Wear high visibility garments. B – know what others are doing.
C – know where others are.
D – all the above.

## Slide 30: GRAPPLE LOADER
There are two types of loaders.
One type is mounted on a truck platform that is mobile.
Another type is loaded on the log truck itself.
The loader operator is limited to one fourth of a circle field of view.
STAY IN THE CLEAR - AWAY from any loading activity.
Notes: Grapple take out , it is self loader! Check each slide term,,

## Slide 31: THE TRUCK MOUNTED GRAPPLE LOADER WHAT YOU NEED TO KNOW 1-materials and logs may fall 2-the loader’s field of vision is only 90° or one fourth of a circle. 3-keep at least two log lengths away from this operation!

## Slide 32: BEWARE OF FALLING LOGS WHAT YOU NEED TO KNOW 1-the grapple may load several logs at once 2-logs can still fall in any direction 3-Keep twice the distance of the log length away.

## Slide 33: SAFETY IN & AROUND EQUIPMENT
CAB ENTRY (3 points of contact)
CAB EXIT (3 points of contact)
YARDERS
Notes: 3 point system

## Slide 34: YARDERS – STAY VISIBLE TO EQUIPMENT OPERATORS WHAT YOU NEED TO KNOW 1-stay in view of the yarder 2-stay in communication

## Slide 35: A SAFE CAB ENTRY WHAT YOU NEED TO KNOW 1-face the cab 2- three points of contact-two hands 1 foot 3-don’t let go.

## Slide 36: AN UNSAFE CAB EXIT WHAT YOU NEED TO KNOW 1-the operator steps out facing forward. 2-stepping down and forward can cause knee injury.

## Slide 37: a safe cab exit WHAT YOU NEED TO KNOW 1-believe it or not, face the cab! 2-three points of contact whenever possible. 3-don’t jump to the ground.

## Slide 38: MAINTENANCE IS IMPORTANT!
IF you work ON, NEAR, or have responsibility for or notice equipment problems, SPEAK UP!
Know what to look for, and you may save someone’s life!
The following contains some useful tips from operators and maintenance professionals.

## Slide 39: HELPFUL TIPS WHEN WORKING ON EQUIPMENT WHAT YOU NEED TO KNOW 1-de-energize. FOLLOW Lockout-Tag out procedure! 2-block up and support any movable part. 3-vent the tank. When working on hydraulics.
Notes: Adjust font

## Slide 40: HARVESTER HEAD - HELPFUL TIPS! WHAT YOU NEED TO KNOW 1-make sure the chain catcher is in place 2-check for hydraulic hose wear. 3-look for frame cracks 4-make sure knives are properly sharpened.

## Slide 41: TIPS ON THE FELLERBUNCHER WHAT YOU NEED TO KNOW 1-teeth should be sharp and properly torqued 2-check for good bearings 3-no slack in the disk 4-good pins and bushings are present 5-no leakage in cylinders.

## Slide 42: SAFETY GLASS IS IMPORTANT ON THE FELLERBUNCHER WHAT YOU NEED TO KNOW 1-window must be safety rated including its replacement 2-must be correct thickness 3-non-shatter window.

## Slide 43: MAINTENANCE IN THE FIELD WHAT YOU NEED TO KNOW 1-Grease it 2-Check hoses 3-Remove debris

## Slide 44: QUICK TEST
Answer this question:
Question: what are some safe operating rules for maintaining equipment?
A – do a pre-start equipment check. B – do maintenance in the field as necessary.
C – have a mechanic do the proper repairs before equipment use.
D – all the above.

## Slide 45: WRAP-UP
Mobile equipment is highly dangerous.
Equipment operators may not always see you.
It is everyone’s responsibility to see each other.
Wear high visibility safety equipment.
Make sure equipment is checked and repairs are completed before proceeding to work.

## Slide 46: OSHA NOTICE & DISCLAIMER
“This material was produced under grant SH20866SH0 from the Occupational Safety and Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government”