## Slide 1: OSHA NOTICE & DISCLAIMER
“This material was produced under grant SH20866SH0 from the Occupational Safety and Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government”

## Slide 2: FELLING SAFELY (Module #2)
REAL Loggers don’t take short cuts!
Trees weigh several thousand pounds!
Directional falling takes advantage of gravity.
Use safe procedures every time!

## Slide 3: TREE FELLING
Most logging is mechanical.
But Cutters/Fallers/Sawyers are involved when needed.
Professional Cutters/Fallers/Sawyers:
ALWAYS wear their Personal Protective Equipment PPE.
Are properly equipped (Wedges, Saws, etc.).
Assess Danger.
Plan and use an Escape Route when needed.

## Slide 4: STEP by STEP – EXAMPLES of PROFESSIONAL LOGGERS
In the next few slides, PROFESSIONAL TIPS will be explained.

## Slide 5: TREE CUTTING WHAT YOU NEED TO KNOW: 1 - Have the RIGHT EQUIPMENT. 2 - CHECK the TREE & AREA. 3 - Plan A Diagonal Escape Path, THEN Make the Cut! 4 - Use Your Escape Path! It’s a SAFETY VIOLATION if you don’t move away!
.

## Slide 6: Tree Cutting
Before felling is started, the Cutter/Faller/Sawyer shall plan and clear a retreat path.
The retreat path extends diagonally AWAY from the expected felling line (unless the retreat path poses a greater hazard than an alternate path).
Once the back cut has been made, IMMEDIATELY MOVE A SAFE DISTANCE AWAY from the tree on the retreat path.
USE AN ESCAPE PATH EVERY TIME – NO EXCEPTIONS!

## Slide 7: SAFE TREE CUTTING REQUIRES PLANNING AND USING AN ESCAPE PATH! WHAT YOU NEED TO KNOW 1 - Determine where the tree will fall. 2 - Plan a Diagonal ESCAPE PATH (45 degrees) AWAY from the direction of Fall! 3 - After making the back cut, IMMEDIATELY Move AWAY from the Stump!

## Slide 8: THE FACE CUT WHAT YOU NEED TO KNOW 1-FACE CUT - Take ¼ of the tree for SMALLER diameter trees, as close to 45 degrees as possible. Usually a Humboldt cut. 2- Take 1/3 of the tree for LARGER diameter trees. 3-Make BACK CUT ABOVE the face cut, a MINIMUM of 1 inch. 4-Leave good HINGEWOOD to avoid tree kick-back!

## Slide 9: CONTROL YOUR AREA WHAT YOU NEED TO KNOW 1- Assess OVERHEAD HAZARDS. 2- Clear area as necessary. 3- Check for and BINDING in each Tree. (Tension & Compression)

## Slide 10: MAKE an ESCAPE PATH WHAT YOU NEED TO KNOW 1- Assess the area and conditions. 2- Plan an escape route – 45 degree angle AWAY from direction of fall - if snow’s in the way, clear a path! 3- USE IT every time.

## Slide 11: MINOR CORRECTIONS
OSHA does not actually “approve” any cutting methods, because they’re not an approving agency.
The Humboldt cut, the conventional cut and the open face cut are the most common safe undercuts to use.
If a tree has a large diameter, wedges must be used.
If the direction of TREE lean is in question, or, if the TREE will fall into a headwind, USE WEDGES!
CHECK with your supervisor for any WEDGE requirements in your state.

## Slide 12: QUICK TEST
Answer this question: Should you always plan an escape route and assess the danger of the tree?
A-YES
B-NO

## Slide 13: WRAP-UP
ALWAYS wear your PPE
MAKE the Right CUT (leave good hinge wood)
PLAN your Escape Route
USE your Escape Route

## Slide 14: OSHA NOTICE & DISCLAIMER
“This material was produced under grant SH20866SH0 from the Occupational Safety and Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government”

## Slide 15: HUMBOLDT CUT – Angle of UNDERCUT as close to 45* as possible.
“This material was produced under grant SH20866SH0 from the Occupational Safety and Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government”