## Slide 1: ERGONOMICS
School of Continuing Education
& Professional Development
Miami Dade College North Campus
OSHA - Susan Harwood Training Grant

## Slide 2: Disclaimer
DISCLAIMER: This material was produced under grant number SH 208 32–SH–0 from the Occupational Safety and Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U. S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U. S. Government. The U.S. Government does not warrant or assume any legal liability or responsibility for the accuracy, completeness, or usefulness of any information, apparatus, product, or process disclosed. COPYRIGHT INFORMATION: This material is the copyrighted property of Miami Dade College. By federal regulation, OSHA reserves a license to use and disseminate such material for the purpose of promoting safety and health in the workplace. Miami Dade College hereby authorizes employers and workplace safety and health professionals to use this material, distributed by or through OSHA, in their workplaces or practices in accordance with the guidance contained in the material. To this end, permission is granted to use such copyrighted material solely for non-commercial, instructional, personal, or scholarly purposes. The material may be used and incorporated into other workplace safety and health programs on the condition that no fee may be charged for the subsequent use of the material. Use of the material for any other purpose, particularly commercial use, without the prior, express written permission of the copyright owner/s is prohibited. Furthermore, any modification to the material is prohibited without the prior, express written permission of the copyright owners.
OSHA - Susan Harwood Training Grant

## Slide 3: Class Overview
Definition of Ergonomics
OSHA Guidelines
Ergonomics Stressors
Common Ergonomic Injuries
Recommended Solutions

## Slide 4: Definition of Ergonomics
Ergonomics –(er-ge-na-miks)–n. Greek term for “the laws of work.”
The science of adapting workstations, tools, equipment and job techniques to be compatible with human anatomy and physiology to reduce the risk of Musculoskeletal Disorder injuries due to Ergonomic Stressors.
In other words, “fit the job to the person” rather than the “person to the job.”

## Slide 5: Defining Musculoskeletal Disorder
Injuries caused by repeated physical trauma or exposure to a specific body part, such as the back, hand, wrist, or forearm
Also called repetitive strain injuries, repetitive motion disorders, overuse syndrome and Cumulative Trauma Disorders (CTDs)
Caused by Ergonomic Stressors

## Slide 6: Common MSDs
Back Injuries
Neck Injuries
Lower Extremities Injuries
Hand Arm Vibration Syndrome
Carpal Tunnel Syndrome

## Slide 7: OSHA Guidelines
Focuses on industries and employers with known high injury and illness rates related to ergonomic hazards.
Coordinates inspections with a legal strategy designed to target prosecutable ergonomic violations.
Serious ergonomics hazards will be addressed using Section 5(a)(1) of the OSH Act, often referred to as the General Duty Clause.

## Slide 8: The General Duty Clause
The General Duty Clause describes the employer's obligation to "furnish to each of his employees employment and a place of employment which are free from recognized hazards that are causing or are likely to cause death or serious physical harm to his employees." This clause from the OSH Act is utilized to cite serious hazards where no specific OSHA standard exists to address the hazard, as is the case with ergonomic stressors.
When OSHA uses the General Duty Clause to cite an employer, OSHA must demonstrate that:
1) The employer failed to keep the workplace free of a hazard to which employees were exposed.
2) The hazard was causing or likely to cause death or serious physical harm.
3) The hazard was recognized.
4) A feasible means of abatement for that hazard exists.

## Slide 9: Current Ergonomics Guidelines
Beverage Distribution
Shipyards
Poultry Processing Plants
Retail Grocery Stores
Nursing Homes
Meatpacking Plants

## Slide 10
Workplace Stressors
Repetitive Motion
  Assembly Line
  Lifting
  Climbing
  Painting
  Typing
  Tool Operations

## Slide 11
Workplace Stressors
Vibration
  Grinders
  Sanders
  Drills
  Chisels
  Chainsaws
  Jackhammers
  Riveters

## Slide 12: Workplace Stressors
Excessive Force
  Lifting
  Pushing
  Pulling
  Moving Heavy Objects

## Slide 13
Workplace Stressors
Awkward Position
  Reaching under
  low Shelves
  Holding object far away from your body
  Painting ceilings

## Slide 14: Conditions Aggravate with:
Age
Stress
Physical Conditioning

## Slide 15: AVERAGE AGE OF ALL U.S. WORKERS

## Slide 16: Our Reaction to Stress
Our bodies first reaction to stress, either
physical or emotional, is muscle tension
(Fight or Flight Syndrome)
A tense muscle is a tight muscle
Tight muscles are much more
susceptible to strains and sprains

## Slide 17: Physical Conditioning
Lack Of Exercise
Poor Nutrition
Poor Sleep
Generally Unhealthy Lifestyle Habits

## Slide 18: The Costs of Injuries
Direct
  Diagnosis
  Surgery
  Rehab
Indirect
  Turnover
  Absenteeism Due to Unreported Injuries
  Ongoing Benefit Costs
  Overtime used to Cover Lost/Restricted Days
  Morale
  Product Damage
  Bureaucratic Costs of Injury/Claims Handling
    Accident Reporting
    Accident Investigation
    Case Management

## Slide 19: SO HOW DO WE PREVENT THESE INJURIES?

## Slide 20
PERSONAL PROTECTIVE EQUIPMENT (PPE)
Clothing or devices worn to help isolate a person from
direct exposure to a hazardous material or situation.
  Back Supports
  Anti-Vibration Gloves
  Wrist Supports
  Wraps & Sleeves

## Slide 21: BACK INJURIES

## Slide 22: DID YOU KNKOW…
The back is the most frequently injured body part. Once injured, the risk of recurrence doubles
Low back injuries represent over 90 percent of all injury claims
Second only to the common cold in terms of lost work days
Back pain cost American businesses an estimated $30 billion each year
Four out of every five people will experience back pain in their lifetimes

## Slide 23: YOUR BACK
The purpose of the back is to support the upper body, protect your spinal cord and allow flexibility
Most of the stress when lifting and bending is absorbed by the lower back. To take some pressure away from the spine, your abdominal and back muscles contract to give added
support
For example, when you lift a load, your abdomen and back muscles help equalize the effort so the entire weight is not transmitted to the spine, but is absorbed in the abdominal cavity. This is called intra-abdominal pressure.

## Slide 24: CAUSES OF BACK INJURY
Improper lifting techniques
Overexertion
Poor posture
Medical factors (age, other disabilities, etc.)
Slips and falls
Excessive weight
Lack of exercise
Stress
Heavy purses and briefcases

## Slide 25: SYMPTONS OF BACK INJURY
Pain
Stiffness
Numbness in the legs
Limited ability to sit or stand
Muscle weakness, spasms and strains
Decreased range of motion

## Slide 26: PROPER LIFTING TECHNIQUES
Squat to lift and lower
Do not bend at the waist
Keep you back straight while
bending over
Keep the weight as close to you as
possible
Bow your back in and raise up with your
head first
If you must turn, turn with your feet, not
your body
Never jerk or twist!
Put the weight down by keeping your low
back bowed in
Keep you feet apart, staggered if possible
Wear shoes with non-slip soles

## Slide 27: BACK INJURY CONTROL
PPE (Personal Protective Equipment)
  Wear a flexible back support for additional lower back and abdominal support
  Back supports also serve as useful reminders to lift properly

## Slide 28: THE BACK SUPPORT

## Slide 29: WHAT IS A BACK SUPPORT?
The back support is a control measure designed to reduce the risk of back injuries. It provides support to the lower back and abdomen by some of stress away from these areas

## Slide 30: WHAT WILL THE BACK SUPPORT DO FOR YOU?
Two things: it will support your lower back and abdomen and it will remind you to use proper lifting techniques
The back support provides lower back and abdominal support when you lift. By tightening the back support you enhance your body’s intra-abdominal pressure and move the stress away from your spine
The back support reminds you to use proper lifting techniques. Every time you tighten the two-stage closure you are telling your body it is time to lift. This action reminds you to think about the Eight Commandments of Lifting, making lifting easier and safer

## Slide 31: WHAT THE BACK SUPPORT WON’T DO FOR YOU?
It won’t cure an existing back problem
It won’t make you a body builder
If you continue to lift large, heavy and bulky objects you have an increased likelihood of injuring yourself

## Slide 32: BACK SUPPORT DEMO
How To Put on Back Support:
  Loosen suspenders and slip on the back support.
  Grasp each end of the waistband. Stretch the right end with hook-and-loop fastener across the left and attach (approximately 4-6 inches [10-15 cm] of overlap). The upper edge of the waistband should be just below the navel. Fasten the outer elastic bands at your side.
  Adjust suspenders for a comfortable fit. For maximum effectiveness, the back support must be properly positioned.
  Before lifting, grasp the outer elastic bands and pull forward as far possible. Secure bands in a comfortable position.
  Loosen when finished with lifting task

## Slide 33: UPPER EXTREMITY INJURIES

## Slide 34: UPPER EXTREMITY INJURIES
Hand-Arm Vibration Syndrome
Carpal Tunnel Syndrome (CTS)

## Slide 35: HAND-ARM VIBRATION SYNDROME (HAVS)
Chronic disorder that can develop when the hand is subjected to repeated and prolonged exposure to vibration
Most often the damage to the blood vessels, nerves and muscles is irreversible
Half of the 1.5 million American workers who use vibrating tools will develop some form of HAVS (NIOSH)
5% of the general population suffers from HAVS
Other term: White Finger

## Slide 36: H.A.V.S. SYMPTOMS AND RISK FACTORS
Symptoms
  Tingling or numbness in fingers and palm
  Spasms in fingers
  Blanching of the fingers
Risk Factors
  Repeated and prolonged exposure to hand-held vibrating tools
  Improper tool use
  Forceful tool grip
  Aggravated by
    Temperature - Cold
    Damp environment
    Smoking

## Slide 38: H.A.V.S. CONTROL
PPE
  Wear full-fingered, certified anti-vibration gloves to reduce exposure to vibration

## Slide 39: DEMONSTRATION

## Slide 40: CARPAL TUNNEL SYNDROME

## Slide 41: CARPAL TUNNEL SYNDROME
Damage to the hands and wrist is one of the fastest growing categories of worker’s compensation claims
Wrist injuries accounted for more than half of all MSDs
Five million American workers suffer from repetitive stress injuries to the wrist

## Slide 42
CARPAL TUNNEL SYNDROME (CTS)
Occurs when the median nerve running through a passage in the wrist up to the hand is compressed and inflamed.

## Slide 43: CARPAL TUNNEL SYNDROME
Causes
  Repetition
  Sustained exertions
  Awkward wrist and
  positions
Symptoms
  Tingling and
  Pain in the hand and
  numbness
  wrist
  Muscle atrophy at base
  of thumb

## Slide 44: CARPAL TUNNEL SYNDROME CONTROL
PPE
  Use a flexible wrist support to encourage neutral wrist posture and limit wrist movements to help reduce the strain and pressure

## Slide 45: DEMONSTRATION

## Slide 46: KEY BENEFITS OF GOOD ERGONOMICS
Reduced worker’s
compensation costs
Reduced absenteeism
Increased
productivity
Increased morale
Increased work
quality

## Slide 47: QUESTIONS?

## Slide 48: THANK YOU!