## Slide 1: Unit 1: Q1
Which of the following is true?
Low pressure spray polyurethane foam chemical health and safety is the main focus of the training.
The training does not provide safety information for two-component high pressure SPF.
Insulating foam sealant, also known as “foam in can” is intended for Do-It-Yourself (DIY) and professional use.
All of the above
Notes: Which of the following is true?
Low pressure spray polyurethane foam chemical health and safety is the main focus of the training.
The training does not provide safety information for two-component high pressure SPF.
Insulating foam sealant, also known as “foam in can” is intended for Do-It-Yourself (DIY) and professional use.
All of the above

## Slide 2: Unit 1: Q1
Which of the following is true?
Low pressure spray polyurethane foam chemical health and safety is the main focus of the training.
The training does not provide safety information for two-component high pressure SPF.
Insulating foam sealant, also known as “foam in can” is intended for Do-It-Yourself (DIY) and professional use.
All of the above
Notes: The correct answer is D. All of the above are true statements regarding this training program.

## Slide 3: Unit 1: Q2
Which of the following weatherization products is not included in this health and safety training?
Insulating foam sealant
Two-component low pressure SPF kits
Fiberglass batt insulation
Low pressure SPF refillable systems
Notes: Which of the following weatherization products is not included in this health and safety training?
Insulating foam sealant
Two-component low pressure SPF kits
Fiberglass batt insulation
Low pressure SPF refillable systems

## Slide 4: Unit 1: Q2
Which of the following weatherization products is not included in this health and safety training?
Insulating foam sealant
Two-component low pressure SPF kits
Fiberglass batt insulation
Low pressure SPF refillable systems
Notes: The correct answer is C. Safety guidance when using fiberglass batt insulation is not included in this training.

## Slide 5: Unit 1: Q3 Debrief
When describing differences between two-component low pressure (LP) SPF and high pressure (HP) SPF, which of the following is not true?
LP SPF is applied in smaller volumes than HP SPF.
LP SPF products use large 55 gallon drums to store A-side and B-side chemicals.
LP SPF is typically sprayed at room temperature, whereas HP SPF is heated to high temperatures (120-150°F) while being sprayed.
LP SPF is pressurized at less than 250 psi, whereas HP SPF is typically pressurized at 1000-1300 psi.
Notes: When describing differences between two-component low pressure (LP) SPF and high pressure (HP) SPF, which of the following is not true?
LP SPF is applied in smaller volumes than HP SPF.
LP SPF products use large 55 gallon drums to store A-side and B-side chemicals.
LP SPF are typically sprayed at room temperature, whereas HP SPF is heated to high temperatures (120-150°F) while being sprayed.
LP SPF is pressurized at less than 250 psi, whereas HP SPF is typically pressurized at 1000-1300 psi.

## Slide 6: Unit 1: Q3 Debrief
When describing differences between two-component low pressure (LP) SPF and high pressure (HP) SPF, which of the following is not true?
LP SPF is applied in smaller volumes than HP SPF.
LP SPF products use large 55 gallon drums to store A-side and B-side chemicals.
LP SPF is typically sprayed at room temperature, whereas HP SPF is heated to high temperatures (120-150°F) while being sprayed.
LP SPF is pressurized at less than 250 psi, whereas HP SPF is typically pressurized at 1000-1300 psi.
Notes: The correct answer is B. Two-component low pressure SPF products do not use large 55 gallon drums to store A-side and B-side chemicals. They are typically packaged in kits which include small cylinders or tanks.

## Slide 7: Unit 1: Q4
____________ are intended for Do-It-Yourself weatherization projects and are widely available at home improvement centers?
High pressure SPF systems
Two-component low pressure SPF kits/refillable systems
Insulating foam sealants or “foam in a can”
Both B and C.
Notes: ____________ are intended for Do-It-Yourself weatherization projects and are widely available at home improvement centers?
High pressure SPF systems
Two-component low pressure SPF kits/refillable systems
Insulating foam sealants or “foam in can.”
Both B and C.

## Slide 8: Unit 1: Q4
____________ are intended for Do-It-Yourselfers (DIYers) and are widely available at home improvement centers?
Two-component high pressure SPF systems
Two-component low pressure SPF kits/refillable systems
Insulating foam sealants or “foam in a can”
Both B and C.
Notes: The correct answer is C. Insulating foam sealants, also known as “foam in can,” are intended for Do-It-Yourself weatherization projects and are widely available at retail home improvement centers.

## Slide 9: Unit 1: Q5 Debrief
Which of the following is true when applying insulating foam sealant?
Read and follow all instructions on the label.
Wear proper protective gear as suggested by the manufacturer including: safety glasses/goggles; gloves and full-coverage clothing.
Open windows and doors to help provide good ventilation as recommended by the manufacturer. Fans may be useful.
All of the above.
Notes: Which of the following is true when applying insulating foam sealant?
Read and follow all instructions on the label.
Wear proper protective gear as suggested by the manufacturer including: safety glasses/goggles; gloves and full-coverage clothing
Open windows and doors to help provide good ventilation as recommended by the manufacturer. Fans may be useful.
All of the above

## Slide 10: Unit 1: Q5 Debrief
Which of the following is true when applying insulating foam sealant?
Read and follow all instructions on the label.
Wear proper protective gear as suggested by the manufacturer including: safety glasses/goggles; gloves and full-coverage clothing.
Open windows and doors to help provide good ventilation as recommended by the manufacturer. Fans may be useful.
All of the above.
Notes: The correct answer is D. All of the above.

## Slide 11: Unit 1: Q6 Debrief
Which of the following is not a typical use for low pressure SPF kits/systems?
Enhancing primary insulation to fill small holes and gaps
Insulating and air sealing attics and crawl spaces
Sealing around rim joists, duct work and pipes
Insulating large roofing surfaces
Notes: Which of the following is not a typical use for low pressure SPF kits/systems?
Enhancing primary insulation to fill small holes and gaps.
Insulating and air sealing attics and crawl spaces.
Sealing around rim joists, duct work and pipes.
Insulating large roofing surfaces.

## Slide 12: Unit 1: Q6 Debrief
Which of the following is not a typical use for low pressure SPF kits/systems?
Enhancing primary insulation to fill small holes and gaps
Insulating and air sealing attics and crawl spaces
Sealing around rim joists, duct work and pipes
Insulating large roofing surfaces
Notes: The correct answer is D. Low pressure SPF is typically not used to insulate large roofing surfaces. High pressure SPF is better suited for those kinds of projects.

## Slide 13: Unit 2: Q1 Debrief
The OSHA Hazard Communication Standard requires employers to have a written program to address:
Labels and other forms of warning
Employee training
Safety Data Sheets (SDS)
All of the above
Notes: The OSHA Hazard Communication Standard requires employers to have a written program to address:
Labels and other forms of warning
Employee training
Safety Data Sheets (SDS)
All of the above

## Slide 14: Unit 2: Q1 Debrief
The OSHA Hazard Communication Standard requires employers to have a written program to address:
Labels and other forms of warning
Employee training
Safety Data Sheets (SDS)
All of the above
Notes: The correct Answer is D. All of the above.

## Slide 15: Unit 2: Q2 Debrief
If an Safety Data Sheet (SDS) is not available for a hazardous chemical on the job site, contact _______ before using the product.
the homeowner
your employer
the building occupants
none of the above
Notes: If an Safety Data Sheet (SDS) is not available for a hazardous chemical on the job site, contact _______ before using the product.
the homeowner
your employer
the building occupants
none of the above

## Slide 16: Unit 2: Q2 Debrief
If an Safety Data Sheet (SDS) is not available for a hazardous chemical on the job site, contact _______ before using the product.
the homeowner
your employer
the building occupants
none of the above
Notes: The correct answer is B. Contact your employer if an Safety Data Sheet or SDS is not available for a hazardous chemical on the job site BEFORE using the product.

## Slide 17: Unit 2: Q3 Debrief
Reading the SDS will help you do all of the following except:
learn the potential hazards of the chemicals you will be handling
determine how far you are willing to travel for an SPF job
choose the correct PPE for the job
understand the proper way to clean up a spill
Notes: Reading the SDS will help you do all of the following except:
learn the potential hazards of the chemicals you will be handling
determine how far you are willing to travel for an SPF job
choose the correct PPE for the job
understand the proper way to clean up a spill

## Slide 18: Unit 2: Q3 Debrief
Reading the SDS will help you do all of the following except:
learn the potential hazards of the chemicals you will be handling
determine how far you are willing to travel for an SPF job
choose the correct PPE for the job
understand the proper way to clean up a spill
Notes: The correct answer is B. Reading the SDS will not help you determine how far you are willing to travel for an SPF job.

## Slide 19: Unit 3: Q1 Debrief
_____ is a possible way a worker can be exposed to a chemical.
Inhalation, or breathing chemical vapors
Skin or eye contact
Ingestion
All of the above
Notes: _____ is a possible way a worker can be exposed to a chemical.
Inhalation, or breathing chemical vapors
Skin or eye contact
Ingestion
All of the above

## Slide 20: Unit 3: Q1 Debrief
_____ is a possible way a worker can be exposed to a chemical.
Inhalation, or breathing chemical vapors
Skin or eye contact
Ingestion
All of the above
Notes: The correct answer is D. All of the above are possible ways a worker can be exposed to a chemical.

## Slide 21: Unit 3: Q2
Which of the following is true about chronic health effects?
Chronic effects are long-term (sometimes permanent) due to repeated exposure to certain chemicals.
Chronic effects usually go away over time.
Chronic effects can occur at chemical concentrations below which short-term effects are experienced.
A and C above.
Notes: Which of the following is true about chronic health effects?
Chronic effects are long-term (sometimes permanent) due to repeated exposure to certain chemicals.
Chronic effects usually go away over time.
Chronic effects can occur at chemical concentrations below which short-term effects are experienced.
A and C above.

## Slide 22: Unit 3: Q2
Which of the following is true about chronic health effects?
Chronic effects are long-term (sometimes permanent) due to repeated exposure to certain chemicals.
Chronic effects usually go away over time.
Chronic effects can occur at chemical concentrations below which short-term effects are experienced.
A and C above.
Notes: The correct answer is D. Both A and C are true about chronic health effects.

## Slide 23: Unit 3: Q3 Debrief
Occupational exposure limits are __________ set by government regulators and expert organizations to protect healthy workers from effects due to chemical exposure.
acceptable odor levels
air concentration levels
frequency and length of employee breaks
all of the above
Notes: Occupational exposure limits are __________ set by government regulators and expert organizations to protect healthy workers from effects due to chemical exposure.
acceptable odor levels
air concentration levels
frequency and length of employee breaks
all of the above

## Slide 24: Unit 3: Q3 Debrief
Occupational exposure limits are __________ set by government regulators and expert organizations to protect healthy workers from effects due to chemical exposure.
acceptable odor levels
air concentration levels
frequency and length of employee breaks
all of the above
Notes: The correct answer is B. Occupational exposure limits are air concentration levels set by government regulators and expert organizations to protect healthy workers from effects due to chemical exposure.

## Slide 25: Unit 3: Q4 Debrief
Which of the following is not true about potential chemical exposure when applying two-component low pressure SPF?
Chronic effects are long-term, sometimes permanent, health effects due to repeated exposure to certain chemicals.
Two-component low pressure kits can release enough chemicals into the air to pose a potential inhalation and/or skin exposure hazard.
It is not necessary to wear personal protective equipment (PPE).
Personal protective equipment that is incorrectly selected or used could lead to chemical exposure.
Notes: Which of the following is not true about potential chemical exposure when applying two-component low pressure SPF?
Chronic effects are long-term, sometimes permanent, health effects due to repeated exposure to certain chemicals.
Two-component low pressure kits can release enough chemicals into the air to pose a potential inhalation and/or skin exposure hazard.
It is not necessary to wear personal protective equipment (PPE).
Personal protective equipment that is incorrectly selected or used could lead to chemical exposure.

## Slide 26: Unit 3: Q4 Debrief
Which of the following in not true about potential chemical exposure when applying two-component low pressure SPF?
Chronic effects are long-term, sometimes permanent, health effects due to repeated exposure to certain chemicals.
Two-component low pressure kits can release enough chemicals into the air to pose a potential inhalation and/or skin exposure hazard.
It is not necessary to wear personal protective equipment (PPE).
Personal protective equipment that is incorrectly selected or used could lead to chemical exposure.
Notes: The correct answer is C. Proper personal protective equipment is required when using two-component low pressure SPF.

## Slide 27: Unit 4: Q1 Debrief
Two-component low pressure SPF kits or systems contain _________ which mix together to make foam when sprayed.
water and adhesives
A-side and B-side chemicals
alcohol and catalysts
none of the above
Notes: Two-component low pressure SPF kits or systems contain _________ which mix together to make foam when sprayed.
water and adhesives
A-side and B-side chemicals
alcohol and catalysts
none of the above

## Slide 28: Unit 4: Q1 Debrief
Two-component low pressure SPF kits or systems contain _________ which mix together to make foam when sprayed.
water and adhesives
A-side and B-side chemicals
alcohol and catalysts
none of the above
Notes: The correct answer is B. Two-component low pressure SPF kits or systems contain A-side and B-side chemicals which mix together to make foam when sprayed.

## Slide 29: Unit 4: Q2 Debrief
The A-side (Iso) of SPF contains _____.
ethanol
polyurethane foam dust
a chemical commonly referred to as “MDI”
a polyol blend
Notes: The A-side (Iso) of SPF contains _____.
ethanol
polyurethane foam dust
a chemical commonly referred to as “MDI”
a polyol blend

## Slide 30: Unit 4: Q2 Debrief
The A-side (Iso) of SPF contains _____.
ethanol
polyurethane foam dust
a chemical commonly referred to as “MDI”
a polyol blend
Notes: The correct answer is C. The A-side (Iso) of SPF contains a chemical commonly referred to as “MDI”.

## Slide 31: Unit 4: Q3 Debrief
Which of the following is not included in the B-side of two-component low pressure SPF?
flame retardant
surfactant
isocyanate
polyol
Notes: Which of the following is not included in the “B-side” of spray polyurethane foam?
flame retardant
surfactant
isocyanate
polyol

## Slide 32: Unit 4: Q3 Debrief
Which of the following is not included in the B-side of two-component low pressure SPF?
flame retardant
surfactant
isocyanate
polyol
Notes: The correct answer is C. Isocyanate is not included in the B-side of spray polyurethane foam.

## Slide 33: Unit 5: Q1 Debrief
Which is a potential effect of A-side (Iso) exposure?
irritation of the eyes
skin irritation
respiratory irritation
all of the above
Notes: Which is a potential effect of A-side (Iso) exposure?
irritation of the eyes
skin irritation
respiratory irritation
all of the above

## Slide 34: Unit 5: Q1 Debrief
Which is a potential effect of A-side (Iso) exposure?
irritation of the eyes
skin irritation
respiratory irritation
all of the above
Notes: The correct answer is D. All of the statements are correct.

## Slide 35: Unit 5: Q2 Debrief
Which statement is true about sensitization to the A-side (Iso)?
It is the development of an unusual sensitivity to a substance resulting in an allergic response after future exposures.
Sensitization may occur following inhalation.
Sensitization may occur following skin contact.
All of the above
Notes: Which statement is true about sensitization to the A-side (Iso)?
It is the development of an unusual sensitivity to a substance resulting in an allergic response after future exposures.
Sensitization may occur following inhalation.
Sensitization may occur following skin contact.
All of the above

## Slide 36: Unit 5: Q2 Debrief
Which statement is true about sensitization to the A-side (Iso)?
It is the development of an unusual sensitivity to a substance resulting in an allergic response after future exposures.
Sensitization may occur following inhalation.
Sensitization may occur following skin contact.
All of the above
Notes: The correct answer is D. All of the statements are correct.

## Slide 37: Unit 5: Q3 Debrief
Respiratory sensitization can lead to asthma, which can be life-threatening. Which of the following symptoms is not a typical symptom of a respiratory sensitization reaction?
blisters forming on the skin
shortness of breath
coughing
chest tightness
Notes: Respiratory sensitization can lead to asthma, which can be life-threatening. Which of the following symptoms is not a typical symptom of a respiratory sensitization reaction?
blisters forming on the skin
shortness of breath
coughing
chest tightness

## Slide 38: Unit 5: Q3 Debrief
Respiratory sensitization can lead to asthma, which can be life-threatening. Which of the following symptoms is not a typical symptom of a respiratory sensitization reaction?
blisters forming on the skin
shortness of breath
coughing
chest tightness
Notes: The correct answer is A. Blisters forming on the skin is not a typical symptom of a respiratory sensitization reaction.

## Slide 39: Unit 5: Q4
_______ is a possible cause of respiratory sensitization.
A single exposure to the A-side (Iso) over the exposure limit without appropriate protection
Repeated unprotected exposure exceeding the exposure limit for the A-side (Iso) without appropriate protection
Repeated unprotected skin contact with A-side chemicals
All of the above
Notes: _____ is a possible cause of respiratory sensitization.
A single exposure to the A-side (Iso) over the exposure limit without appropriate protection
Repeated unprotected exposure exceeding the exposure limit for the A-side (MDI) without appropriate protection
Repeated unprotected skin contact with A-side chemicals
All of the above

## Slide 40: Unit 5: Q4
_______ is a possible cause of respiratory sensitization.
A single exposure to the A-side (Iso) over the exposure limit without appropriate protection
Repeated unprotected exposure exceeding the exposure limit for the A-side (Iso) without appropriate protection
Repeated unprotected skin contact with A-side chemicals
All of the above
Notes: The correct answer is D, all of the above.

## Slide 41: Unit 5: Q5 Debrief
If diagnosed with sensitization to the A-side (Iso), contact your healthcare provider. You may be ____________.
instructed not to work with isocyanates
asked to stop lifting heavy spray foam equipment
instructed to temporarily isolate yourself from others until the sensitization clears up
none of the above
Notes: If diagnosed with sensitization to the A-side (Iso), contact your healthcare provider. You may be ____________.
instructed not to work with isocyanates
asked to stop lifting heavy spray foam equipment
instructed to temporarily isolate yourself from others until the sensitization clears up
none of the above

## Slide 42: Unit 5: Q5 Debrief
If diagnosed with sensitization to the A-side (Iso), contact your healthcare provider. You may be ____________.
instructed not to work with isocyanates
asked to stop lifting heavy spray foam equipment
instructed to temporarily isolate yourself from others until the sensitization clears up
none of the above
Notes: The correct answer is A. You may be instructed not to work with isocyanates if you are diagnosed with sensitization to the A-side (Iso).

## Slide 43: Unit 6: Q1 Debrief
The B-side is a blend of chemicals with the main ingredient being polyols. Which of the following is not a typical B-side additive?
catalyst
fire retardant
acetone
blowing agent
Notes: The B-side is a blend of chemicals with the main ingredient being polyols. Which of the following is not a typical B-side additive?
catalyst
fire retardant
acetone
blowing agent

## Slide 44: Unit 6: Q1 Debrief
The B-side is a blend of chemicals with the main ingredient being polyols. Which of the following is not a typical B-side additive?
catalyst
fire retardant
acetone
blowing agent
Notes: The correct answer is C. Acetone is not a typical B-side chemical ingredient.

## Slide 45: Unit 6: Q2 Debrief
Which of the following is not a potential effect of eye exposure to some catalysts in the B-side?
reddening or burning
near-sightedness
a blue haze or halovision
tearing
Notes: Which of the following is NOT an effect of eye exposure to some catalysts in the B-side?
reddening or burning
near-sightedness
a blue haze or halovision
tearing

## Slide 46: Unit 6: Q2 Debrief
Which of the following is not a potential effect of eye exposure to some catalysts in the B-side?
reddening or burning
near-sightedness
a blue haze or halovision
tearing
Notes: The correct answer is B. Near-sightedness is not an effect of eye exposure to some B-side catalysts.

## Slide 47: Unit 6: Q3 Debrief
Which symptom is a potential effect of exposure to the B-side?
skin irritation
eye irritation
respiratory irritation
all of the above
Notes: Which symptom is a potential effect of exposure to the B-side?
skin irritation
eye irritation
respiratory irritation
all of the above

## Slide 48: Unit 6: Q3 Debrief
Which symptom is a potential effect of exposure to the B-side?
skin irritation
eye irritation
respiratory irritation
all of the above
Notes: The correct answer is D. All of the above.

## Slide 49: Unit 7: Q1 Debrief
Which of the following best describes engineering controls?
control switches on high-tech spray foam equipment
changes in the design of the job, such as containment and ventilation, to reduce the potential for chemical exposure
recommended spraying techniques to maximize product performance
D. all of the above
Notes: Which of the following best describes engineering controls?
control switches on high-tech spray foam equipment
changes in the design of the job, such as containment and ventilation, to reduce the potential for chemical exposure
recommended spraying techniques to maximize product performance
all of the above

## Slide 50: Unit 7: Q1 Debrief
Which of the following best describes engineering controls?
control switches on high-tech spray foam equipment
changes in the design of the job, such as containment and ventilation, to reduce the potential for chemical exposure
recommended spraying techniques to maximize product performance
D. all of the above
Notes: The correct answer is B. Engineering controls are changes in the design of the job, such as containment and ventilation, to reduce the potential for chemical exposure.

## Slide 51: Unit 7: Q2 Debrief
When is the best time to plan engineering controls?
soon after spraying your first low pressure kit so you are familiar with the job
before beginning work
at the end of the first day
none of the above
Notes: When is the best time to plan engineering controls?
soon after spraying your first low pressure kit so you are familiar with the job
before beginning work
at the end of the first day
none of the above

## Slide 52: Unit 7: Q2 Debrief
When is the best time to plan engineering controls?
soon after spraying your first low pressure kit so you are familiar with the job
before beginning work
at the end of the first day
None of the above
Notes: The correct answer is B. The best time to plan engineering controls is before beginning work.

## Slide 53: Unit 7: Q3
When selecting engineering controls prior to SPF application, which of the following is not a jobsite factor to consider?
indoor or outdoor work?
brand of drywall in the building?
amount of natural ventilation available?
occupied building vs. vacant building?
Notes: When selecting engineering controls prior to SPF application, which of the following is not a jobsite factor to consider?
indoor or outdoor work?
brand of drywall in the building?
amount of natural ventilation available?
occupied building vs. vacant building?

## Slide 54: Unit 7: Q3
When selecting engineering controls prior to SPF application, which of the following is not a jobsite factor to consider?
indoor or outdoor work?
brand of drywall in the building?
amount of natural ventilation available?
occupied building vs. vacant building?
Notes: The correct answer is B. The brand of drywall is not a jobsite factor to consider when planning and selecting engineering controls prior to SPF application.

## Slide 55: Unit 7: Q4 Debrief
Weatherization projects may take place in confined spaces, such as attics and crawl spaces. Which of the following is not true?
Use best efforts to ventilate confined spaces.
A respirator is unnecessary when spraying a two-component low pressure SPF kit in a confined space.
Fans can help improve ventilation and disperse vapors.
Consult the SPF product manufacturer to determine how long to ventilate the spray area after spraying has stopped.
Notes: Weatherization projects may take place in confined spaces, such as attics and crawl spaces. Which of the following is not true?
Use best efforts to ventilate confined spaces.
A respirator is unnecessary when spraying a two-component low pressure SPF kit in a confined space.
Fans can help improve ventilation and disperse vapors.
Consult the SPF product manufacturer to determine how long to ventilate the spray area after spraying has stopped

## Slide 56: Unit 7: Q4 Debrief
Weatherization projects may take place in confined spaces, such as attics and crawl spaces. Which of the following is not true?
Use best efforts to ventilate confined spaces.
A respirator is not necessary when spraying a two-component low pressure SPF kit in a confined space.
Fans can help improve ventilation and disperse vapors.
Consult the SPF product manufacturer to determine how long to ventilate the spray area after spraying has stopped.
Notes: The correct answer is B. Proper personal protective equipment, including an approved respirator, is recommended when spraying a two-component low pressure SPF kit in a confined space.

## Slide 57: Unit 8: Q1 Debrief
Which of the following is a topic to discuss when reviewing the safety plan with the homeowner or building manager and other workers?
Who will be on the job site?
What safety measures will be taken?
When does the product manufacturer recommend that homeowners or occupants can re-enter after spraying is completed?
All of the above
Notes: Which of the following is a topic to discuss when reviewing the safety plan with the homeowner or building manager and other workers?
Who will be on the job site?
What safety measures will be taken?
When does the product manufacturer recommend that homeowners or occupants can re-enter after spraying is completed?
All of the above

## Slide 58: Unit 8: Q1 Debrief
Which of the following is a topic to discuss when reviewing the safety plan with the homeowner or building manager and other workers?
Who will be on the job site?
What safety measures will be taken?
When does the product manufacturer recommend that homeowners or occupants can re-enter after spraying is completed?
All of the above
Notes: The correct answer is D. All of the above topics are important to discuss when reviewing the safety plan.

## Slide 59: Unit 8: Q2 Debrief
How long should you typically wait before allowing an occupant to re-enter following an interior two-component low pressure SPF application?
until all of the foam dust has settled
consult the manufacturer since re-entry time can vary (some manufacturers recommend a one hour re-entry time)
one week
48 hours
Notes: How long should you typically wait before allowing an occupant to re-enter following an interior two-component low pressure SPF application?
until all of the foam dust has settled
consult the manufacturer since re-entry time can vary (some manufacturers recommend a one hour re-entry time)
one week
48 hours

## Slide 60: Unit 8: Q2 Debrief
How long should you typically wait before allowing an occupant to re-enter following an interior two-component low pressure SPF application?
until all of the foam dust has settled
consult the manufacturer since re-entry time can vary (some manufacturers recommend a one hour re-entry time)
one week
48 hours
Notes: The correct answer is B. Consult the product manufacturer for guidance on when to allow occupants to re-enter following an interior two-component low pressure SPF application. Although re-entry time can vary depending on a number of factors, some manufacturers recommend a one hour re-entry time.

## Slide 61: Unit 8: Q3 Debrief
_____________ is an example of how to prepare the spray area before applying of two-component low pressure SPF.
Applying engineering controls, such as containment and ventilation
Shutting off ignition sources
Protecting surfaces from potential overspray
All of the above
Notes: _____________ is an example of how to prepare the spray area before applying of two-component low pressure SPF.
Applying engineering controls, such as containment and ventilation
Shutting off ignition sources
Protecting surfaces from potential overspray.
All of the above

## Slide 62: Unit 8: Q3 Debrief
_____________ is an example of how to prepare the spray area before applying of two-component low pressure SPF.
Applying engineering controls, such as containment and ventilation
Shutting off ignition sources
Protecting surfaces from potential overspray
All of the above
Notes: The correct answer is D. All of the above are examples of how to prepare the spray area before applying two-component low pressure SPF.

## Slide 63: Unit 8: Q4
It is not important to know the location of ____________ when applying two-component low pressure SPF at a jobsite.
Safety Data Sheets for all chemicals on the job
a first aid kit
a discount high pressure SPF product supplier in the area
a fire extinguisher
Notes: It is not important to know the location of ____________ when applying two-component low pressure SPF at a jobsite.
Safety Data Sheets for all chemicals on the job
a first aid kit
a discount high pressure SPF product supplier in the area
a fire extinguisher

## Slide 64: Unit 8: Q4
It is not important to know the location of ____________ when applying two-component low pressure SPF at a jobsite.
Safety Data Sheets for all chemicals on the job
a first aid kit
a discount high pressure SPF product supplier in the area
a fire extinguisher
Notes: The correct answer is C. It is not important to know the location of a discount high pressure SPF product supplier in the area when you are applying two-component low pressure SPF at the jobsite.

## Slide 65: Unit 9: Q1
Refer to _____ for information on appropriate Personal Protective Equipment (PPE) for the chemicals with which you will be working.
your coworker
the Safety Data Sheet (SDS)
your customer
none of the above
Notes: Refer to _____ for information on appropriate Personal Protective Equipment (PPE) for the chemicals with which you will be working.
your coworker
the Safety Data Sheet (SDS)
your customer
none of the above

## Slide 66: Unit 9: Q1
Refer to _____ for information on appropriate Personal Protective Equipment (PPE) for the chemicals with which you will be working.
your coworker
the Safety Data Sheet (SDS)
your customer
None of the above
Notes: The correct answer is B. The Safety Data heet provides information about PPE for the chemicals with which you will be working.

## Slide 67: Unit 9: Q2 Debrief
  Typical PPE worn during two-component low pressure SPF application includes _____.
  protective clothing and gloves
  protective clothing, gloves and hearing protection
  hearing protection and respiratory protection
  protective clothing, gloves, eye protection, and respiratory protection
Notes:   Typical PPE worn during two-component low pressure SPF application includes _____.
  protective clothing and gloves
  protective clothing, gloves and hearing protection
  hearing protection and respiratory protection
  protective clothing, gloves, eye protection, and respiratory protection

## Slide 68: Unit 9: Q2 Debrief
  Typical PPE worn during two-component low pressure SPF application includes _____.
  protective clothing and gloves
  protective clothing, gloves and hearing protection
  hearing protection and respiratory protection
  protective clothing, gloves, eye protection, and respiratory protection
Notes:   The correct answer is D. Typical PPE worn during two-component low pressure SPF application includes protective clothing, gloves, eye protection, and respiratory protection.

## Slide 69: Unit 9: Q3
Applicators typically wear hooded disposable coveralls when applying SPF. If clothing comes in contact with liquid SPF chemicals (A-side and/or B-side), it is best to __________.
dispose of the clothing
air it out to dry
wait a week before wearing it again
use a spot cleaner on the contaminated areas
Notes: Applicators typically wear hooded disposable coveralls when applying SPF. If clothing becomes contaminated with SPF chemicals, it is best to __________.
dispose of the clothing
air it out to dry
wait a week before wearing it again
use a spot cleaner on the contaminated areas

## Slide 70: Unit 9: Q3
Applicators typically wear hooded disposable coveralls when applying SPF. If clothing comes in contact with liquid SPF chemicals (A-side and/or B-side), it is best to __________.
dispose of the clothing
air it out to dry
wait a week before wearing it again
use a spot cleaner on the contaminated areas
Notes: The correct answer is A. If clothing becomes contaminated with SPF chemicals, dispose of the clothing. Do not wear contaminated clothing home.

## Slide 71: Unit 9: Q4 Debrief
The following statements regarding respirator use when applying two-component low pressure SPF are true, except:
Manufacturers recommend that you wear an appropriate air-purifying respirator (APR) anytime you are spraying two-component low pressure SPF.
Gloves and protective clothing are not needed when wearing an air-purifying respirator (APR).
Types of respirators commonly used for two-component low pressure application include half-face APRs, full-face APRs and powered air-purifying respirators (PAPRs).
OSHA established a Respiratory Protection Standard to regulate the use of respirators in the workplace.
Notes: The following statements regarding respirator use when applying two-component low pressure SPF are true, except:
Manufacturers recommend that you wear an appropriate air-purifying respirator (APR) anytime you are spraying two-component low pressure SPF.
Gloves and protective clothing are not needed when wearing an air-purifying respirator (APR).
Types of respirators commonly used for two-component low pressure application include half-face APRs, full-face APRs and powered air-purifying respirators (PAPRs).
OSHA established a Respiratory Protection Standard to regulate the use of respirators in the workplace.

## Slide 72: Unit 9: Q4 Debrief
The following statements regarding respirator use when applying two-component low pressure SPF are true, except:
Manufacturers recommend that you wear an appropriate air-purifying respirator (APR) anytime you are spraying two-component low pressure SPF.
Gloves and protective clothing are not needed when wearing an air-purifying respirator (APR).
Types of respirators commonly used for two-component low pressure application include half-face APRs, full-face APRs and powered air-purifying respirators (PAPRs).
OSHA established a Respiratory Protection Standard to regulate the use of respirators in the workplace.
Notes: The correct answer is B. Gloves and protective clothing ARE required when wearing an air-purifying respirator (APR).

## Slide 73: Unit 9: Q5 Debrief
Air-purifying respirator (APR) and powered air-purifying respirator (PAPR) cartridges are changed out _____ to prevent chemical breakthrough.
when they develop an unpleasant odor
annually
according to the employer’s cartridge change out schedule
once a month
Notes: APR and PAPR cartridges are changed out _____ to prevent chemical breakthrough.
when they develop an unpleasant odor
annually
according to the employer’s cartridge change out schedule
once a month

## Slide 74: Unit 9: Q5 Debrief
Air-purifying respirator (APR) and powered air-purifying respirator (PAPR) cartridges are changed out _____ to prevent chemical breakthrough.
when they develop an unpleasant odor
annually
according to the employer’s cartridge change out schedule
once a month
Notes: The correct answer is C. Air-purifying respirator and powered air-purifying respirator cartridges are changed out according to the employer’s cartridge changeout schedule to prevent chemical breakthrough.

## Slide 75: Unit 9: Q6 Debrief
  When wearing a tight-fitting respirator, a respirator user conducts a user seal check _________.
  each time the respirator is worn
  weekly
  annually
  only if multiple users share the respirator
Notes:   When wearing a tight-fitting respirator, a respirator user conducts a user seal check _________.
  each time the respirator is worn
  weekly
  annually
  only if multiple users share the respirator

## Slide 76: Unit 9: Q6 Debrief
  When wearing a tight-fitting respirator, a respirator user conducts a user seal check _________.
  each time the respirator is worn
  weekly
  annually
  only if multiple users share the respirator
Notes:   The correct answer is A. A user seal check, both positive and negative pressure, is conducted each time the respirator is worn.

## Slide 77: Unit 10: Q1 Debrief
For specific first aid instructions for the chemical with which you will be working, ________.
refer to the Safety Data Sheet (SDS)
ask your co-worker
do a computer search on the topic of first aid for chemical exposure
none of the above
Notes: For specific first aid instructions for the chemical with which you are working, _____.
refer to the Safety Data Sheet (SDS)
ask your co-worker
do a computer search on the topic of first aid for chemical exposure
none of the above

## Slide 78: Unit 10: Q1 Debrief
For specific first aid instructions for the chemical with which you will be working, ________.
refer to the Safety Data Sheet (SDS)
ask your co-worker
do a computer search on the topic of first aid for chemical exposure
none of the above
Notes: The correct answer is A. Refer to the Safety Data Sheet for specific first aid instructions for the chemical with which you will be working.

## Slide 79: Unit 11: Q1 Debrief
Which of the following is not true about thermal decomposition that can potentially occur when SPF is overheated?
Heat given off during curing can result in possible scorching, smoldering and fire.
Low pressure spray polyurethane foam will not burn.
Smoke and vapors may be produced.
SPF is formulated with flame retardants to meet building codes.
Notes: Which of the following is not true about thermal decomposition that can potentially occur when SPF is overheated?
Heat given off during curing can result in possible scorching, smoldering and fire.
Low pressure spray polyurethane foam will not burn.
Smoke and vapors may be produced.
SPF is formulated with flame retardants to meet building codes.

## Slide 80: Unit 11: Q1 Debrief
Which of the following is not true about thermal decomposition that can potentially occur when SPF is overheated?
Heat given off during curing can result in possible scorching, smoldering and fire.
Low pressure spray polyurethane foam will not burn.
Smoke and vapors may be produced.
SPF is formulated with flame retardants to meet building codes.
Notes: The correct answer is B. Spray polyurethane foam can burn if it is overheated.

## Slide 81: Unit 11: Q2 Debrief
Which of the following is true regarding techniques to help prevent thermal decomposition of SPF?
Keep the foam cool by turning up the fans.
Follow manufacturer’s recommendation on lift thickness and time between lift/pass.
Apply the foam in as thick a lift as possible.
None of the above
Notes: Which of the following is true regarding techniques to help prevent thermal decomposition of SPF?
Keep the foam cool by turning up the fans.
Follow the manufacturer’s recommendation on lift thickness and time between lift/pass.
Apply the foam in as thick a lift as possible.
None of the above

## Slide 82: Unit 11: Q2 Debrief
Which of the following is true regarding techniques to help prevent thermal decomposition of SPF?
Keep the foam cool by turning up the fans.
Follow manufacturer’s recommendation on lift thickness and time between lift/pass.
Apply the foam in as thick a lift as possible.
None of the above
Notes: The correct answer is B. To prevent thermal decomposition, follow the manufacturer’s recommendation on lift thickness and time between lift/pass.

## Slide 83: Unit 12: Q1 Debrief
If a spill does occur, which of the following is an appropriate action to take?
Identify the spilled material.
Refer to the manufacturer’s instructions and Safety Data Sheet (SDS) for guidance on clean up.
With your employer’s permission, consider cleaning up the spill if it is a manageable quantity and you have appropriate training.
All of the above
Notes: If a spill does occur, which of the following is an appropriate action to take?
Identify the spilled material.
Refer to the manufacturer’s instructions and Safety Data Sheet (SDS) for guidance on clean up.
With your employer’s permission, consider cleaning up the spill if it is a manageable quantity and you have appropriate training.
All of the above

## Slide 84: Unit 12: Q1 Debrief
If a spill does occur, which of the following is an appropriate action to take?
Identify the spilled material.
Refer to the manufacturer’s instructions and Safety Data Sheet (SDS) for guidance on clean up.
With your employer’s permission, consider cleaning up the spill if it is a manageable quantity and you have appropriate training.
All of the above.
Notes: The correct answer is D. All of the above are appropriate actions to take in the event of a spill.

## Slide 85: Unit 12: Q2 Debrief
PPE typically worn when cleaning up a chemical spill includes all of the following except:
chemical-resistant gloves
hearing protection
eye protection
protective clothing
Notes: PPE typically worn when cleaning up a chemical spill includes all of the following except:
chemical-resistant gloves
hearing protection
eye protection
protective clothing

## Slide 86: Unit 12: Q2 Debrief
PPE typically worn when cleaning up a chemical spill includes all of the following except:
chemical-resistant gloves
hearing protection
eye protection
protective clothing
Notes: The correct answer is B. PPE typically worn when cleaning up a chemical spill includes chemical resistant gloves, eye protection and protective clothing. Respiratory protection also may be needed in certain instances. Always refer to the SDS for guidance.

## Slide 87: Unit 13: Q1 Debrief
The following is true regarding low pressure SPF canister/cylinder storage except:
Store at temperatures consistent with manufacturer’s instructions.
Store insulating foam sealant cans or low pressure SPF kits in an upright position.
Avoid puncturing the can or cylinder.
The cans/cylinders are non-pressurized so there is no risk of explosion.
Notes: The following is true regarding low pressure SPF canister/cylinder storage except:
Store at temperatures consistent with manufacturer’s instructions.
Store insulating foam sealant cans or low pressure SPF kits in an upright position.
Avoid puncturing the can or cylinder.
The cans/cylinders are non-pressurized so there is no risk of explosion.

## Slide 88: Unit 13: Q1 Debrief
The following is true regarding low pressure SPF can/cylinder storage except:
Store at temperatures consistent with manufacturer’s instructions.
Store insulating foam sealant cans or low pressure SPF kits in an upright position.
Avoid puncturing the can or cylinder.
The cans/cylinders are non-pressurized so there is no risk of explosion.
Notes: The correct answer is D. Low pressure SPF ingredients are pressurized in the cans or cylinders.

## Slide 89: Unit 13: Q2 Debrief
___________ may be disposed of as non-hazardous household waste in accordance with federal, state and local regulations.*
55 gallon drums used for high pressure SPF chemical storage
Empty insulating foam sealant cans
Partially used two-component low pressure SPF cylinders/tanks
All of the above
* Disposal regulations are subject to change.
Notes: ___________ may be disposed of as non-hazardous household waste in accordance with federal, state and local regulations.
55 gallon drums used for high pressure SPF chemical storage
Empty insulating foam sealant cans
Partially used two-component low pressure SPF cylinders/tanks
All of the above

## Slide 90: Unit 13: Q2 Debrief
___________ may be disposed of as non-hazardous household waste in accordance with federal, state and local regulations.*
55 gallon drums used for high pressure SPF chemical storage
Empty insulating foam sealant cans
Partially used two-component low pressure SPF cylinders/tanks
All of the above
* Disposal regulations are subject to change.
Notes: The correct answer is B. Empty insulating foam sealant cans may be disposed of as non-hazardous household waste in accordance with federal, state and local regulations.

## Slide 91: Unit 13: Q3 Debrief
Do not abandon or leave behind cylinders or tanks of unreacted chemicals from a low pressure kit or system. Dispose of waste chemicals in accordance with _____ regulations.*
federal
state
local
all of the above
* Disposal regulations are subject to change.
Notes: Do not abandon or leave behind cylinders or tanks of unreacted chemicals from a low pressure kit or system. Dispose of waste chemicals in accordance with _____ regulations.
federal
state
local
all of the above

## Slide 92: Unit 13: Q3 Debrief
Do not abandon or leave behind cylinders or tanks of unreacted chemicals from a low pressure kit or system. Dispose of waste chemicals in accordance with _____ regulations.*
federal
state
local
all of the above
* Disposal regulations are subject to change.
Notes: The correct answer is D. All of the above. Dispose of waste chemicals in accordance with federal, state, and local regulations.

## Slide 93: Unit 14: Q1 Debrief
A unique safety challenge when applying two-component low pressure SPF in a confined space (i.e. attic or crawlspace) is ____________.
SPF vapors may not dissipate as quickly since air movement is limited (the use of fans can help move vapor away from the applicator)
ventilation may be limited (proper PPE, including an approved respirator is required)
entry and exit points may be more restricted (keeping these areas free of equipment and debris is very important)
all of the above
Notes: A unique safety challenge when applying two-component low pressure SPF in a confined space such as an attic or crawlspace, is ____________.
SPF vapors may not dissipate as quickly since air movement is limited (the use of fans can help move vapor away from the applicator).
ventilation may be limited (proper PPE, including an approved respirator is required)
entry and exit points may be more restricted (keeping these areas free of equipment and debris is very important)
all of the above

## Slide 94: Unit 14: Q1 Debrief
A unique safety challenge when applying two-component low pressure SPF in a confined space (i.e. attic or crawlspace) is ____________.
SPF vapors may not dissipate as quickly since air movement is limited (the use of fans can help move vapor away from the applicator)
ventilation may be limited (proper PPE, including an approved respirator is required)
entry and exit points may be more restricted (keeping these areas free of equipment and debris is very important)
all of the above
Notes: The correct answer is D. All of the above pose unique safety challenges when applying two-component low pressure SPF in a confined space, such as an attic or crawlspace.

## Slide 95: Unit 14: Q2
____________ are the leading cause of fatalities in the construction industry according to the Bureau of Labor Statistics.
Heart attacks due to physical exertion
Falls
Electrocutions
None of the above
Notes: ____________ are the leading cause of fatalities in the construction industry according to OSHA.
Heart attacks due to physical exertion
Falls
Electrocutions
None of the above

## Slide 96: Unit 14: Q2
____________ are the leading cause of fatalities in the construction industry according to the Bureau of Labor Statistics.
Heart attacks due to physical exertion
Falls
Electrocutions
None of the above
Notes: The correct answer is B. Falls are the leading cause of fatalities in the construction industry according to OSHA.

## Slide 97: Unit 14: Q3 Debrief
The following are ways to help prevent potential injuries from slips and falls except:
Ladders and scaffolding must be constructed and used in accordance with OSHA standards.
Elevated work must comply with OSHA fall protection requirements.
Do not use eye protection when applying spray polyurethane foam so your visibility is better.
Keep the worksite clean and free of tripping hazards.
Notes: The following are ways to help prevent potential injuries from slips and falls except:
Ladders and scaffolding must be constructed and used in accordance with OSHA standards.
Elevated work must comply with OSHA fall protection requirements.
Do not use eye protection when applying spray polyurethane foam so your visibility is better.
Keep the worksite clean and free of tripping hazards.

## Slide 98: Unit 14: Q3 Debrief
The following are ways to help prevent potential injuries from slips and falls except:
Ladders and scaffolding must be constructed and used in accordance with OSHA standards.
Elevated work must comply with OSHA fall protection requirements.
Do not use eye protection when applying spray polyurethane foam so your visibility is better.
Keep the worksite clean and free of tripping hazards.
Notes: The correct answer is C. Whenever you apply SPF, eye protection is required. Be sure that your eye protection is well maintained and provides good visibility while applying the foam.

## Slide 99: Unit 14: Q4 Debrief
Which of the following is not a way to help avoid heat stress?
Provide adequate ventilation through the use of fans and by opening windows and doors.
Drink plenty of beverages that contain alcohol or caffeine.
Consider wearing a loose-fitting, hooded powered air-purifying respirator which can circulate cool air to the user.
Schedule frequent rest periods in shaded or air conditioned areas.
Notes: Which of the following is NOT a way to help avoid heat stress?
Provide adequate ventilation through the use of fans and by opening windows and doors.
Drink plenty of beverages that contain alcohol or caffeine.
Consider wearing a loose-fitting, hooded powered air-purifying respirator which can circulate cool air to the user.
Schedule frequent rest periods in shaded or air conditioned areas.

## Slide 100: Unit 14: Q4 Debrief
Which of the following is not a way to help avoid heat stress?
Provide adequate ventilation through the use of fans and by opening windows and doors.
Drink plenty of beverages that contain alcohol or caffeine.
Consider wearing a loose-fitting, hooded powered air-purifying respirator which can circulate cool air to the user.
Schedule frequent rest periods in shaded or air conditioned areas.
Notes: The correct answer is B. Avoid drinking beverages that contain alcohol or caffeine. However, it is a good idea to drink fluids often and before you are thirsty.