## Slide 1
This material was produced under grant number SH-22316-SH-1 from the Occupational Safety and Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government.
Safe Patient Handling: Recommended Best Practices
Presented By The University of Texas-School of Public Health

## Slide 2: Learning Objectives
By the end of this module participants should be able to:
Describe the elements of OSHA and NIOSH’s Safe Patient Handling Programs.
Identify appropriate techniques and strategies for safe patient handling practices.
Describe how elements of this program can be incorporated into the participant’s inpatient nursing unit.

## Slide 3: Background
Nurses and Nurses’ Aides are at high risk for work-related back pain
  Nurses’ aides at higher risk for work-related back pain compared to nurses
  Perform more lifting, bending and twisting in their jobs
Nurses, nurses’ aides and orderlies among those most likely to lose time from work due to work-related back pain
  Aides and orderlies have higher lost workday injury rates compared to nurses
References: Bureau Labor Statistics, 2005; Engkvist et al., 2000; Fuortes et al. 1994; Guo et al., 1995; Videman et al., 1984

## Slide 4: Mechanics of Patient Handling Tasks
Patient transfers
  one-person (hug) vs. two-person (gait belt)
  bed-wheelchair, bed-commode, commode-chair
Repositioning
  one-person vs. two-person
  hook method, draw sheet, lift under thigh, and shoulder
None of the techniques assessed sufficiently protect patient handlers
All tasks exceed spinal load limits recommended by NIOSH (Marras et al. 1999)

## Slide 5: Study Findings
Pompeii et al.
Musculoskeletal Injuries Resulting From Patient Handling Tasks Among Hospital Workers. American Journal of Industrial Medicine

## Slide 6
Injury Claims Resulting from Patient Handling Nurses and Nurses’ Aides (n = 630)
Chart: 
| Lifting Patient | Pull-Up in Bed | Transfer Patient | Reposition Patient | Caught Patient | Transport in Bed/Chair | Assist
Series 1 | 0.22 | 0.17 | 0.13 | 0.13 | 0.05 | 0.1 | 0.2
1997-2003

## Slide 7: What is “Best Practice” Patient Handling?
VA – Audrey Nelson
OSHA
NIOSH
AOHP
Washington State – OSHA
(copies are provided)

## Slide 8: Elements of a ‘Best Practice’ Patient Handling Program –VA (1)
Ergonomic Assessment Protocol:
  Assess the hospital environment, examine injury rates, identify high-risk units
Patient Assessment Criteria
  Tools to help nurses evaluate patient characteristics that affect decision making about equipment and techniques for safe patient handling
Algorithms for Patient Handling/Movement
  Standardized processes for making decisions about the equipment and the number of staff necessary to perform high-risk activities safely.

## Slide 9: Elements of a ‘Best Practice’ Patient Handling Program –VA (2)
Selection of patient handling equipment (mechanical, non-mechanical)
  Ensuring that the right equipment is available in sufficient quantities, kept in convenient locations, and in operating condition
BIRNs-Back Injury Resource Nurses
  Peers selected for high-risk nursing units who are specially trained in the identification of workplace hazards, in the criteria for assessing safe patient handling and movement, and in the use of algorithms. The role also includes onsite training and evaluation of peers regarding the proper use of equipment
“After Action Review”
  Knowledge the team has gained by performing a task in one setting and how it is applied in a different setting

## Slide 10: Elements of a ‘Best Practice’ Patient Handling Program –VA (3)
“No-Lift Policy” or “Minimal Manual Lift Policy"
  Establishes an agreement among staff members that they will use the safest approach to handling and moving patients
  Indicates support from management that safe patient handling practices should be used

## Slide 11
Patient Assessment Criteria
  Tools to help nurses evaluate patient characteristics that affect decision making about equipment and techniques for safe patient handling

## Slide 13
Algorithms for Patient Handling/Movement
  Standardized processes for making decisions about the equipment and the number of staff necessary to perform high-risk activities safely.

## Slide 17
Selection of patient handling equipment (mechanical, non-mechanical)
  Ensuring that the right equipment is available in sufficient quantities, kept in convenient locations, and in operating condition

## Slide 18: Equipment at St. Luke’s
Gait Belt
Draw Sheet
Hoyer Lift
Slide Board

## Slide 19: Draw Sheet
http://www.youtube.com/watch?v=GABAUWN27Yg

## Slide 20: Gait Belts

## Slide 21: Barton Chair
http://www.youtube.com/watch?v=BQbCp_QSwio

## Slide 22: Hovertech: Hovermatt

## Slide 23: Hovertech: Hoverjack

## Slide 24: Hoyer Lift
http://www.youtube.com/watch?v=DinUBHOBlWU

## Slide 25: Slippery Sally Roller Slide Board
http://www.youtube.com/watch?v=QS-qjcgkk6E
Sally Roller Slide Board
http://www.slipperysally.com.au/sallyroller

## Slide 26: ARJO: Maxi Move (1)

## Slide 27: ARJO: Maxi Move (2)

## Slide 28: Overhead/Ceiling Lift
ARJO Maxi Sky-
Available in Various Weight Requirements

## Slide 29: ARJO: Sara 3000 (Sit to Stand)
http://www.youtube.com/watch?v=XJu8p4r13WU

## Slide 30: Hovertech: Sit to Stand

## Slide 31: ARJO: Sara Plus

## Slide 32: ARJO: SARA STEDY
Transfer aid

## Slide 33: Plastic Liner/Slip Resistant Sheet
http://www.youtube.com/watch?v=RH-gsrUwLrA

## Slide 34: Draw Sheet with Handles

## Slide 35: Elements of a ‘Best Practice’ Patient Handling Program –VA
BIRNs-Back Injury Resource Nurses
  Peers selected for high-risk nursing units who are specially trained in the identification of workplace hazards, in the criteria for assessing safe patient handling and movement, and in the use of algorithms. The role also includes onsite training and evaluation of peers regarding the proper use of equipment
“After Action Review”
  Knowledge the team has gained by performing a task in one setting and how it is applied in a different setting

## Slide 36: Research: Evaluation of “Best Practice” Program Elements
Evidence Tables
  Biomechanical Studies
  Primary Evaluation of Multifaceted Programs that include patient handling equipment
  Systematic Reviews

## Slide 37: Primary Evaluation Studies (1)
13 Studies Examined Multiple “Best Practice” Program Elements
  Overhead Lifts in long-term care facilities were most effective at reducing the risk of injury.
  The combination of mechanical lift equipment and training was most effective at reducing injuries and lost workdays in the hospital setting.
  Refresher training improves/sustains adoption of safe patient handling practices.
  Some studies found the use of algorithms to guide staff in deciding which transferring and/or lifting method (equipment) to use were effective.

## Slide 38: Primary Evaluation Studies (2)
  Lift Teams were not effective as the only method for addressing patient handling requirements, nursing staff did not want to wait for a Lift Team member to show up to do the task.

## Slide 39: Adoption of Safe Patient Handling Practices: What Research Tells Us
Prior studies have reported promising results of reduction of patient handling injuries when patient handling equipment was used (Owen et al., 2002; Evanoff et al., 2003; Engvist et al., 2000; Byrnes et al., 2004).
Regardless of outcome, all of these studies reported that barriers in the work process hindered adoption of patient handling equipment use.

## Slide 40: Barriers to Equipment Use and Other Best Practices
Lack of knowledge on how to use equipment
Infrequent training
Poor accessibility of equipment
Lack of perceived need
Lack of time to use equipment
Lack of staff to assist with patient moves/transfers
Lack of motivation on the part of staff
Lack of policy (no lift/minimal lift)
Rapid changing patient population disrupts implementation of intervention programs
Patients may act negatively to towards it

## Slide 41: Promoters to Equipment Use and Other Best Practices
Management involvement and support
Combination of equipment, training and procedures to assess patient mobility needs
Good communication with staff about the patient handling program
Unit champions (sometimes this includes nurses who have been previously injured)
Assessment of equipment that fits the patient handling needs of the patient population.
Training, training, training!

## Slide 42: Unit-level implementation
Equipment and overhead supply cabinet (not shown) are locked to prevent items from disappearing.

## Slide 43: Equipment is Inaccessible

## Slide 44: Nursing Culture
Patient handling is part of the job
Hands-on care is a valued part of the job
New nurses want to “fit in”
Social pressure to get job done quickly

## Slide 45
“A Bad System Will Defeat A Good Person Every Time”
- W. Edwards Deming

## Slide 46: Summary
One-Size Fits All is not a feasible approach to developing
a unit level Best Practice Patient Handling Program
This summary provides elements of proposed Best Practice only
It is best to pick elements of these proposed programs that best
Fit the patient handling needs of your patient population
Select elements that can be incorporated and tailored to fit your
unit

## Slide 47: Thank You