## Slide 1
Notes: INSTRUCTOR NOTE: This module should be presented by a knowledgeable, experienced and trained instructor with experience in grain handling and storage, as well as the OSHA grain handling standard.
This module & the accompanying video are based on FEDERAL OSHA regulations. States governed by OSHA approved state plans have OSHA-approved job safety and health programs operated by individual states instead of federal OSHA. Some of their regulations may differ. It is up to the instructor to inform participants of the differences or to warn participants some regulations may differ and they should check with their state regulations.

## Slide 2: PREVENTIVE MAINTENANCE BUCKET ELEVATORS

## Slide 3: Introduction
This Preventive Maintenance for Bucket Elevators module is part of a curriculum series that addresses hazards found in areas of grain handling facilities including grain bins and their surrounding area. It’s purpose is to assist participants to identify and abate hazards in the work place.
Notes: Explain this module is part of a series.
Other modules
  Overview of Grain Handling Safety and Storage (introductory module)
  Lock out Tag out mini module
  Entanglement Hazards and Guarding
  Falls
  Grain Bin Entry
  Lifeline Protection System
  Characteristics of Confined Spaces (in Agriculture)

## Slide 4: Disclaimers
This material was produced under grant number SH-22288SH1 from the Occupational Safety and Health Administration, U. S. Department of Labor.
It does not necessarily reflect the views or policies of the U. S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U. S. Government.
Notes: Instructor Notes:
Explain – GHSC received funding from OSHA. In order to comply with the grant we do need them to sign in and need to collect the following information:
  Supervisor or worker. This information is for statistical purposes to show the types of population receiving training.
  Employer. This is to establish an employer/employee relationship as covered under OSHA. Volunteer rescue workers who may be attending should list their employer; not the volunteer rescue squad. Farmers should list the registered business name of their farm. Farm employees should provide the business name listed on their paycheck.
OSHA does NOT contact the employer.
GHSC may contact the attendee or employer for follow-up evaluation in compliance with grant requirements.

## Slide 5: Employee Rights
Employees are entitled to safe and healthy working conditions which DO NOT pose a risk of serious harm.
Workers are entitled to be fairly compensated for all hours worked in accordance with the law.
Notes: Explain - All DOL grants require that employees are informed of their rights. In this instance we want to emphasize employees are entitled to a safe and healthy working environment AND to fair receive compensation for their work.
Remind employees – it is the employee’s responsibility to follow the safety practices, policies, and procedures of their employers.
Tell participants their rights also include the right to report unsafe conditions to the OSHA hotline without retribution.
More information about employee rights can be found on the OSHA website: www.osha.gov or the Department of Labor website www.dol.gov .
NOTES:
It is ESPECIALLY imperative for youth/young workers to access information and know their rights, what to expect, and how to get help if needed.

## Slide 6: Employer Responsibility
Employers have the responsibility to provide a safe workplace.
More information about employer & employee rights can be found at www.osha.gov.
Notes: Explain employers have a legal responsibility to provide a safe workplace. This means they must ensure the regulations which govern their business are instituted and followed. This applies to 1 employee or more.
Discuss - It is the employers’ responsibility to know the rules and laws – federal and state.
Emphasize – It is employers’ responsibility to ensure employees, know, understand and follow regulations and company policies.
Stress - If employers are unsure of the regulations they should consult with the appropriate agency. Every state has an on-site consultation program jointly funded by OSHA and the state which provides assistance in learning and complying to the regulations.
The OSHA website provides contact information for each state’s on-site consultation program.
Illinois Department of Labor has the on-site consultation program in Illinois.
Employers should also know and understand the state’s laws as they may be more restrictive than OSHA. Contact the state department of labor.

## Slide 7: Learning Objectives
At the end of this module, participants will be able to:
Understand basic preventive maintenance procedures for bucket elevators.
Identify components requiring inspection or maintenance.
Notes: Introduce the learning objectives. These are the knowledge the participant should acquire as well as tasks or skills they should learn to perform.
Explain – the module was designed to seek interaction from the participants. Questions will be asked throughout to generate discussion.
Encourage – the sharing of ideas, information, experiences so everyone can learn.

## Slide 8: PREPARE & CONDUCT PREVENTIVE MAINTENANCE

## Slide 9: Preventive Maintenance
Timely & Properly
Prevents ignition sources
Protects
  Workers
  Product
  Equipment
Often overlooked – something goes wrong
  Less caution
Notes: Legs are the work horses of the grain elevator – carrying and moving hundreds of thousands or millions of bushels of product each year.
Being in good working condition is essential to efficient, productive, and profitable operations.
Scheduled, preventive maintenance is often overlooked or put aside until something goes wrong.
Unscheduled work stoppage – in any industry – leads to a more hurried, less cautious approach putting workers at risk of forgetting or bypassing safety measures.
Preventive maintenance of bucket elevator legs is crucial to controlling ignition sources. Most fires and/or explosions at grain storage facilities occur when some component of the conveying system becomes overheated due to friction.
As on-site storage gets larger it will become more critical for farms to use the same precautions and safety measures as the commercial industry.
Using a scheduled maintenance plan, reduces work stoppages, protects workers, can aid in better storage quality of the product and protects the equipment from unnecessary and often destructive wear/tear.

## Slide 10: Lock out/Tag out before work
Motor drive to conveyor
Clamp/secure belt
Notes: Prior to working on energized Bucket Elevator where contact with the belt, buckets, rotating parts, or electricity is possible:
Lockout/tagout the drive motor to the conveyor.
Prior to splitting a belt or working on a belt that could spin due to gravity**: Clamp or otherwise secure the belt from spinning.
This is usually for major maintenance and not something you would need to do for a regular inspection. If gravity can be a hazard – then secure the belt.

## Slide 11: Label & guard inspection doors
Warning labels
Guard mesh - Behind door
  Open without tool
Guarded
Unguarded
Guarded
Notes: Verify warning labels are on all inspection doors.
Verify Inspection doors with wing nuts, spring clamps, etc.…that don’t require tools to open have guard mesh behind them.
Sign photo: Design ©Clarion Safety Systems. All rights reserved. www.clarionsafety.com. (written permission)

## Slide 12: BELT & BUCKET INSPECTION

## Slide 13: Observe a complete loop
Start at splice or mark
Start at Splice
Starting mark
Notes: Observe the belt and buckets through a complete loop.
Start at the splice or another “mark” so you know you have inspected all.

## Slide 14: Slowly rotate belt
Variable speed drive
  guarded
Creep drive
Move manually
Set Variable Speed Drive
Manual – use bar
Notes: Move with variable speed drive if equipped (should be guarded), or
Move with a creep drive if equipped

## Slide 15: Look front/back for wear & tear
View of Belt - Open Door
Guarded door -variable speed drive
Notes: Belt Inspection
Look at front of belt
Look at back of belt
Inspect for wear
Inspect for tears

## Slide 16: Belt centered in casing
Centered in casing
Cracks, rubbing
Separation, bubbling
Missing, worn, loose bolts
Begin to wear – sharp edges
Check Alignment
View Belt
Sharp edges
Notes: Belt Inspection
Inspect for severe cracks, rubbing, separation, and bubbling
Look for missing, worn, or loose bolts
Check for centering of the belt in the casing. Out of align increases wear & friction

## Slide 17: Belt material is conductive
Verify belt material is conductive
Surface electrical resistance ≤ 300 megaohms
Notes: Belt Inspection
Verify belt is of the correct material
1910.272(q)(2)
All belts and lagging purchased after March 30, 1988 shall be conductive. Such belts shall have a surface electrical resistance not to exceed 300 megohms.

## Slide 18: Inspect buckets for unusual wear
Inspect
  Missing/loose nuts & bolts
  Cracked, broken, loose buckets
  Wear patterns & level
Research unusual wear
  Indicate wear point in casing
Missing Nuts & Loose Buckets
Notes: Bucket Inspection
  Look for missing bolts/Nuts
  Look for loose bolts/Nuts
  Look for cracked, broken, or missing buckets
  Look for wear patterns and wear level
  Research unusual wear marks, scrapes, etc… that indicate a wear point in casing

## Slide 19: Missing buckets
Not blocking discharge spout
Check bucket catcher on discharge spout
Bucket Catching Bars at Discharge
Buckets Caught on Bars
Notes: Bucket Inspection - If missing buckets verify they are not blocking discharge spout.
Check bucket catcher on discharge spout if equipped.

## Slide 20: Belt Tear Views

## Slide 21: PVC Belt Deterioration

## Slide 22: Back side wear examples

## Slide 23: Back side wear on belts

## Slide 24: Cracked/broken buckets

## Slide 25: Bucket inspection issues
Crack
Missing bucket

## Slide 26: Signs of wear - friction

## Slide 27: BELT SPLICES

## Slide 28: 3 types of belt splices
Lap
Butt
Mechanical
Mechanical Splice

## Slide 29: Lap & Butt splice
Torque nuts
Verify bolt condition
Review belt condition
Bolts pulling through belt splice
Notes: Lap and butt Splice
Torque the Nuts to manufacturer’s specifications
Verify bolt condition
Review belt condition as discussed earlier

## Slide 30: Ensure overlap on splices
Bucket overlap
Lap ≥ 6-8
Butt ≥ 12-14
Double Overlap ≥ 12-14
Pulley Side
Pulley Side
Pulley Side
Notes: There should be at least 6-8 buckets worth of overlap on lap splices. 12-14 buckets worth of overlap on Butt or Double Lap. Some recommend 16.

## Slide 31: Nuts & bolts of splicing
Best - Large flange nut, no extra washer
Double nut - serrated flange & fender washer
Avoid small flange nuts & separate fender washer
Notes: Large flange nuts with no extra washer are the preferred connector.
Small flange nuts with separate fender washers have a history of working loose.
If you have serrated flange nuts and fender washers on your splice make sure to double nut them.

## Slide 32: Mechanical splice inspection
Torque nuts
Inspect metal pieces
Belt material at bend
  Verify ‘AB’ non-ferrous
Check Torque of Nuts
Mechanical Splice
Notes: Mechanical Splice
Torque the Nuts to manufacturer’s specifications.
Inspect the condition of metal pieces.
Inspect the belt material at the bend of the splice.
Verify “AB” Non-ferrous.

## Slide 33: Use template for clamp spacing
Incorrectly installed ferrous splice. Clamp spacing too far apart
Use template
Follow manufacturer specification
Notes: Picture of ferrous splice not installed correctly.
Spacing of clamps is too far apart.
Follow manufacturer specification and use template.
On picture - Should Have Used The Template That Comes From Manufacturer of The Splice. Wrong Spec. of Material.

## Slide 34: Torn splices
Torn lap splice
Torn mechanical splice
Torn lap splice

## Slide 35: KNEE PULLEY INSPECTION

## Slide 36: Knee Pulley – Inspect all parts
Bearings
Pulley
Conduit & bearing sensors
Guarding
Check Lock Collar
Tighten Bearing Mount Use a fitted wrench)
Knee Pulley Fully Guarded
Notes: Verify guarding is complete and secure
Check conduit and bearing sensors

## Slide 37: Knee pulley bearing: look , listen
Visually inspect
  infrared
Listen to it run
Lubricate
  Grease purges
Notes: While running listen to the bearing.
Visually inspect bearing. Use infrared if available to check bearing
Lubricate bearings until grease begins to purge from the bearings

## Slide 38: Knee Pulley - tighten bearing parts
Check Lock Collar
Tighten Bearing Mount
(Use fitted wrench)
Notes: Check bearing lock collar bolts for tightness.
Tighten bearing mounts. It is better to use a fitted wrench.

## Slide 39: Pulley Inspection
Knee pulley enclosure opened for inspection
Check Bushing Nuts
Check Pulley Face
Look for wear, cracks, etc.
Notes: Inspect the pulley for general condition (wear, cracks, etc.).
Verify bolt tightness on bushings

## Slide 40: Damaged knee pulley

## Slide 41: Rub blocks must make contact
Placement - belt/pulley contacts rub block
  Check Wiring
Inspection Door
Hanging off mount
Catches pulley, belt movement
Notes: Inspect for placement to make sure the belt and/or pulley will contact the rub block
Inspect wiring
Inspect for wear
  Wear dead center is the worst
  Replace if worn more than ½ through or if worn at center
  Replace if worn to where it doesn’t protect side casing

## Slide 42: Rub block – center wear is worst
Wear - dead center is worst
Replace
  Worn > ½ through or at center
  Doesn’t protect side casing
Worn Rub Block Needs Replaced
Notes: Inspect for placement to make sure the belt and/or pulley will contact the rub block
Inspect wiring
Inspect for wear
  Wear dead center is the worst
  Replace if worn more than ½ through or if worn at center
  Replace if worn to where it doesn’t protect side casing

## Slide 43: Will rub sensor catch future rub?
old rub mark

## Slide 44: Test rub block sensor
Test sensor - use manufacturer’s tester
Alternative - freeze spray
  Monitor readout shows temperature drop
Freeze spray on rub block
Watch display change
Notes: Test sensor
Use manufacturer’s tester if they have one
Another method is to spray with freeze spray
Verify temperature monitor readout shows a drop in temperature

## Slide 45: Inspect casing for alignment
Wear points; signs of rubbing
  Use infrared
Signs of settling/out of alignment
Using infrared to look for rubs
Rusted casing & failing supports
Notes: Inspect for wear points
Inspect for signs of rubbing
Infrared is a great tool
Inspect for signs of settling/out of alignment issues

## Slide 46: EXPLOSION VENTS

## Slide 47: Explosion vents correctly set-up
Remove shipping bolts
Correct bolts & washers
Not blocked from release
Warning labels
Safety catch cables/straps
Missing bolts
Top of Leg Explosion Vent
Notes: Inspect for general condition
Inspect to make sure shipping bolts removed
Inspect to make sure correct bolts and washers in place
Verify it is not blocked from being released
Verify they have warning labels
Verify any safety catch cables or straps are in place
LEFT PICTURE – EXPLOSION VENT AT THE TOP OF THE LEG
RIGHT PICTURE– MISSING EXPLOSION VENT BOLTS

## Slide 48: Must remove shipping bolts
Shipping Bolts Still on Explosion Vent (You Can See The Labels Broke Off Before The Bolts Were Removed)
Warning labels to remove shipping bolts
Must remove shipping bolts before placing into service.
Shipping bolts not removed
Labels missing
Notes: Notice Stickers Warning To Remove Shipping Bolts Before Placing In Service
Shipping Bolts Still on Explosion Vent (You Can See The Labels Broke Off Before The Bolts Were Removed)

## Slide 49: HEAD SECTION INSPECTION

## Slide 50: Check for blockage in discharge
Discharge & wiper plate
  Clearance - ¼ to ½ inch
Plug switch
  Activate; ensure monitor picks up signal
Discharge Throat
Wiper Plate
Wiper Plate in Discharge
Notes: Inspect discharge for condition and potential blockage
Inspect discharge Wiper plate
  Measure clearance of discharge plate 1/4-1/2 inch
Inspect plug switch if equipped
  Verify general condition
  Activate and make sure monitor picks up the signal

## Slide 51: Lining intact & secure to casing
Missing Tiles
Intact Tiles
Inspect lining of head section
Notes: Inspect lining
  Condition
  Secure to casing
  All intact

## Slide 52: Replace worn bucket catchers
Replace bucket catchers before they fail and get into product stream
Good bars on bucket catchers
Notes: Inspect bucket catchers for wear if equipped
Replace before they could fail and get into the product stream

## Slide 53: Lagging should be tight to pulley
Inspect lagging on head pulley
Wear
Tight to pulley
Conductive
Grooves clean, free of material
Notes: Inspect lagging on head pulley
  For wear
  Is it tight to pulley
  Proper type
  Make sure the groves in the lagging are clean
  and free of material

## Slide 54: Worn, slick, damaged lagging

## Slide 55: Head pulley properly aligned
Inspect head pulley
Alignment
  Side to side
  Front to back
General condition
  Face & sides
Measure crown
Check bushing tightness on shaft
Notes: Inspect head pulley
  Inspect alignment side to side and front to back (track measurements for comparison)
Inspect general condition
  Look at face and sides
Can measure crown if tracking is an issue
Check bushing tightness on shaft if accessible

## Slide 56: Head Pulley
Cracked pulley
Check the crown
Head Section Open for Drive Replacement

## Slide 57: Inspect & lubricate bearings
Tighten Mounts
Tighten Collar
Grease Bearing
Bearings tight to shaft
Lubricate
  Manufacturer specs
Notes: Inspect bearings
Inspect bearings tight to shaft
Bearing sensors attached to bearings
Lubricate per manufacturer’s spec

## Slide 58: Ensure belt alignment centered
Inspect alignment
Belt centered
No signs of rubbing
Can See Alignment in Casing
Notes: Inspect alignment
Belt should be centered
No signs of rubbing

## Slide 59: Head section bearing sensors
Inspect bearing sensors – use infrared
  Proper mounting
  Wires intact
  Manufacturer’s tester or freeze spray
Freeze Spray
Disconnected Wire
Check Bearing with infrared camera
Notes: Inspect bearing sensors in head section – use infrared camera if available
Proper mounting – attached to bearings
Wires intact
Use manufacturer’s tester if they have one
Another method is to spray with freeze spray - Verify temperature monitor readout shows a drop in temperature.

## Slide 60: Inspect electrical – head section
Undamaged, sealed, secured conduit
Sealed motor conduit box
Proper rated conduit
Conduit open
Non-sealed
motor conduit box
Notes: Inspect Electrical
  Undamaged and sealed conduit
  Sealed motor conduit box
  Proper rated conduit
  Secured conduit

## Slide 61: Inspect drive – oil & drain vents
Oil level - signs of oil leakage
Drain vents clean
Oil Leak
Notes: Inspect Drive
Oil level
Signs of oil leakage
Drain vents clean

## Slide 62: Inspect drive
Coupler condition
  Lubricate
Sheaves/Sprockets
  secure to shafts
  free from wear & in alignment
Worn Sprockets & Couplers
Worn Coupler
Notes: Coupler
  Lubricate coupler per manufacturer’s recommendation
  Condition of coupler
Sheaves/Sprockets secure to shafts
Sheaves/Sprockets free from wear and in alignment

## Slide 63: Head section drive alignment
Basic alignment
  belt pulleys alignment if equipped
Check belts, tightness & condition
  measure belt deflection
Use String to Check Alignment
Check Belt
Notes: Basic alignment
Check alignment of belt pulleys if equipped. Use string – hold taught.
Check belts, tightness and condition (measure belt deflection)
Inspect Drive

## Slide 64: Grid style coupler inspection
Annual maintenance
Remove cover assembly
Check alignment
Torque all fasteners per spec
Inspect seal ring & gasket
  Replace leaking/worn
Notes: Grid Style Coupler if equipped
  Inspect by removing the cover assembly.
  Check alignment
  Torque all fasteners per spec.
  Inspect seal ring and gasket, replace if leaking or worn.
  Remove the grid spring or grid spring segments
  Thoroughly clean all components.
  Remove both drain plugs and fill with new lube. Grease should purge out the opposite hole. Use long term grease per manufacturer’s specification.
  Pack the grid teeth in the hubs and install grid spring or grid spring segments
  Frequency – annual maintenance

## Slide 65: Grid style coupler inspection
Remove grid spring/grid spring segments
Thoroughly clean all components
Remove both drain plugs; fill
  Grease purges out opposite hole
Pack grid teeth in hubs; install grid
  Use long term grease per manufacturer’s specification

## Slide 66: Para flex coupler inspection
Inspect guard
  2”-3” minimum clearance guard to coupler
  Protects work area
Periodically inspect coupler
  Wear, dust/dirt buildup, impede heat dissipation
Inspect increased levels of vibration/noise
Notes: Para flex Coupler if equipped
Inspect the guard
  2” clearance minimum from guard to coupler (<14” coupler)
  3” clearance minimum from guard to coupler (>14” coupler)
  Able to protect work area if coupler breaks apart
Couplings should be periodically inspected for normal wear, dust/dirt buildup or any similar scenario that would impede heat dissipation.
Increasing levels of vibration and noise could indicate the need for inspection, repair or replacement of the coupling or element.

## Slide 67: Gear coupler annual maintenance
Check alignment per manual
Torque all fasteners
Inspect seal ring & gasket
Re-lubricate coupler
  Apply grease - both sides of coupler through lube plug holes
  leave opposite side open as a vent
  use recommended long-term grease
Notes: Gear Coupler if equipped (annual maintenance)
Check alignment per manual
Torque all fasteners
Inspect seal ring and gasket to determine if replacement is needed.
Re-lubricate coupler. Apply grease to both sides of coupler through lube plug holes leaving opposite side open as a vent (Grease type is important – using recommended long-term grease is preferred by manufacturer – using general purpose grease cuts maintenance interval to ½ the normal maintenance period)

## Slide 68: Gear coupler
General purpose grease cuts maintenance interval to 1/2 the normal maintenance period
Notes: Gear Coupler if equipped (annual maintenance)
Check alignment per manual
Torque all fasteners
Inspect seal ring and gasket to determine if replacement is needed.
Re-lubricate coupler. Apply grease to both sides of coupler through lube plug holes leaving opposite side open as a vent (Grease type is important – using recommended long-term grease is preferred by manufacturer – using general purpose grease cuts maintenance interval to ½ the normal maintenance period)

## Slide 69: Inspect head section motor
Electrical connections
  sealed, tight, complete
Physical condition
Signs of oil leakage
Motor Conduit Box Not Dust Tight
Leg Motor
Proper rating
Secure mounting
Basic alignment
Notes: Inspect Motor
Electrical Connections sealed, tight and complete
Cleanliness
Physical condition
Signs of oil leakage
Proper rating
Grease or Don’t grease depending on company or manufacturer recommendation
Secure mounting
Basic alignment
Motor cooling fan in place, clean, guarded, and operating
Motor cooling fan is not cracked
Sheaves secure to shafts
Sheaves free from wear and in alignment

## Slide 70: Inspect head section motor
Grease – as recommended by manufacturer
Motor cooling fan
  In place, clean, operating, no cracks
  Guarded
Sheaves secure to shafts
  Free from wear
  In alignment
Notes: Inspect Motor
Electrical Connections sealed, tight and complete
Cleanliness
Physical condition
Signs of oil leakage
Proper rating
Grease or Don’t grease depending on company or manufacturer recommendation
Secure mounting
Basic alignment
Motor cooling fan in place, clean, guarded, and operating
Motor cooling fan is not cracked
Sheaves secure to shafts
Sheaves free from wear and in alignment

## Slide 71: Sample - greasing motor bearings
Lockout motor
Remove drain plug
Inspect grease drain
  Use mechanical probe to remove blockages
Add 20 pumps new NLGI No. 2 grease - grease inlet
  Use hand operated grease gun
continued
Notes: Sample Motor Bearing Greasing Instructions
Lockout motor.
Remove the drain plug
Inspect grease drain and remove any blockage with a mechanical probe.
Add 20 pumps of new NLGI No. 2 grease at the grease inlet using a hand operated grease gun.
Run the motor for 15-30 minutes with the drain plug removed to allow purging of any excess grease.
Shut off motor and lockout.
Replace the drain plug.
Return motor to service.

## Slide 72: Sample - greasing motor bearings
Run motor 15-30 minutes
  Drain plug removed
  Purges excess grease
Shut off motor & lockout
Replace drain plug
Return motor to service
Follow manufacturer’s instructions for your installation.
Notes: Sample Motor Bearing Greasing Instructions
Lockout motor.
Remove the drain plug
Inspect grease drain and remove any blockage with a mechanical probe.
Add 20 pumps of new NLGI No. 2 grease at the grease inlet using a hand operated grease gun.
Run the motor for 15-30 minutes with the drain plug removed to allow purging of any excess grease.
Shut off motor and lockout.
Replace the drain plug.
Return motor to service.

## Slide 73: Inspect guarding - head section
Ensure guards – complete, secure, painted, not rubbing
Complete guarding
Incomplete guarding

## Slide 74: BOOT SECTION INSPECTION

## Slide 75: Inspect tail pulley
Tail pulley - sides & face
  Pulley clearance to side of leg casing
  Hub
Bearing Sensor and Bearing
Tail Pulley in Bad Shape
Worn/damaged tail pulleys
Notes: Inspect tail pulley(sides and face)
Inspect pulley clearance to side of leg casing
Inspect bearings
Inspect bearing tightness to shaft and mount
Clean and Inspect boot, look for debris
Clean out all dust and grain residue (for maintenance and sanitation reasons)
Identify source of foreign debris if possible
Verify operation of boot cleanout slide

## Slide 76: Tail pulley - look for cracked hub
Cracked hub on tail pulley
Most common location
Other common area – at edge near face

## Slide 77: Tail pulley bearing
Inspect bearings
Bearing tightness to shaft and mount
Bearing & Bearing Sensor

## Slide 78: Inspect boot section of leg
Clean & Inspect boot
  Look for debris
Clean out all dust & grain residue
  Maintenance & sanitation
  Identify source of foreign debris
Verify operation of boot cleanout slide
Notes: Clean and Inspect boot, look for debris
  Clean out all dust and grain residue (for maintenance and sanitation reasons)
  Identify source of foreign debris if possible
Verify operation of boot cleanout slide

## Slide 79: Inspect monitoring components
Inspect plug switch (if equipped)
  Verify general condition
  Activate & ensure monitor picks up signal
Inspect bearing monitors
  Same as head section
Inspect rub blocks
  Same as head section
Bearing Sensor & Speed Sensor
Notes: Inspect plug switch (if equipped)
  Verify general condition
  Activate and make sure monitor picks up the signal
Inspect bearing monitors -Same as head section
Inspect any rub blocks - Same as head section

## Slide 80: Speed sensors - <20% reduction
Speed sensor – visual inspection
  Mounted on center of shaft
  Wiring & conduit intact
Test
  manufacturer specification or other method
Shut down equipment - belt speed reduced ≤ 20% of normal operating speed
Verify other plant interlocking is functioning
Notes: Inspect Speed sensors (Will vary by style)
General visual inspection
Mounted on center of the shaft
Wiring and conduit intact
Test per manufacturer specification or other suitable method
Verify it shuts equipment down when the belt speed is reduced by no more than 20% of the normal operating speed.
Verify other plant interlocking is functioning

## Slide 81: Inspect take –up mechanism
Mechanical or manual
Frame not bent
Condition of threads
Properly sealed
Measure amount of adjustment left
  Track information
  re-splice belt before adjustment runs out
Mechanical Take-Up
Notes: Inspect take-up mechanism (Mechanical or Manual)
Measure amount of take-up adjustment that is left. Track this information so you can re-splice belt before adjustment runs out
Verify take-up frame is in good shape and not bent
Verify condition of threads on take-up
Verify take-up is properly sealed and not creating a housekeeping issue

## Slide 82: Inspect take-up mechanism
Weighted or Gravity
Frame not bent
Weight stack & support mechanism
  Moves freely
Properly sealed
Measure adjustment amount left & track
Weighted Take-Up
Notes: Inspect take-up mechanism (Weighted or Gravity)
Measure amount of take-up adjustment that is left. Track this information so you can re-splice belt before adjustment runs out
Verify take-up frame is in good shape and not bent
Verify condition weight stack and support mechanism and that it can move freely
Verify take-up is properly sealed and not creating a housekeeping issue

## Slide 83: Look for bent take up mechanism
All take-ups - look for bending, binding, signs of over-stress, etc.
Bent Weighted Take-Up
Bent Weighted Take-Up

## Slide 84: Tracking – center of casing
Observe belt running empty & then full
Watch for tracking in center of casing
  Remain toward center
  Not within inch of casing
Belt Tracking to the Left
Notes: Observe belt running
Should be done empty. Then observe full.
Watch for tracking in the center of the casing. Should remain towards the center and not within an inch of the casing.

## Slide 85: Lubrication- rotate bearing if safe
Grease rotating bearing
Clean tip of zerk & grease gun
Pump grease into zerk
  fresh clean grease purges under & past seal lip
Clean up excess grease
  Repeat as continues to purge
Grease Bearing
Blue Grease Begins to purge
Notes: Grease bearings while bearing is rotating if it is safe to do so.
Clean tip of zerk and grease gun.
Pump proper grease into zerk until fresh clean grease is seen purging under and past the seal lip.
Clean up excess grease that is around the bearing.
May need to come back and clean up grease again as it continues to purge.

## Slide 86: Excess Grease
Need to Clean Up Grease

## Slide 87: Excess Grease examples
shaft is too long requires guard

## Slide 88: Grease leg bearings
Leg bearings - little grease vs high-speed
Manufacturer chart - RPM & run hours
Lubricate before start-up idle equipment
Stay consistent - do not mix greases
  Manufacturer’s recommended or similar
Lower quantity grease frequent intervals more effective
  Vs greater quantity at extended intervals.
Notes: Usually leg bearings are considered slow moving and require little grease compared to high-speed bearings.
  Manufacturer will have a greasing chart based off of RPM and run hours.
  Usually monthly is adequate when in operation for busy locations
Always lubricate prior to start-up any idled equipment
Use manufacturer’s recommended grease or similar. Stay consistent, do not mix greases.
Generally, a lower quantity of grease at frequent intervals is more effective than a greater quantity at extended intervals.

## Slide 89: Gear Box – annual oil check
Change oil annually
  Send oil samples; follow tribology report
  Install drain valves - sampling & draining
  Follow manufacturer recommendation
Drain valve to drain & get sample
Use pump to pull oil samples
Notes: Gear Boxes
  Change Oil Annually, Or
  send oil samples in annually and follow recommendations from tribology report.
  Follow manufacturer recommendation if different from above.

## Slide 90: Magnet inspection
LOTO & wear gloves
Visually inspect
Clean surface
  Analyze debris
Test magnet strength
  Semi-annual
  Pull tester or informal with hand tool
Return to operating condition
  Seal edges - dust control
Determine cleaning frequency
Notes: Lockout hazardous equipment and Wear gloves
Visually inspect for worn spots, physical damage, improper position, un-level condition, etc…
Clean surface and put debris in container for analysis and disposal
Inspect debris to determine if it originated from your facility
Test strength of magnet (informally with a hand tool or formally with pull tester) (semi-annual recommended)
Return to operating condition and usually seal the edges for dust control
Reanalyze frequency of cleaning based on findings.

## Slide 91: Pull Testing – magnet strength
Clean magnet surface
Select test piece, spacers
  Use same equipment
Zero scale
Attract piece to magnet - center
Pull scale perpendicular to surface
  Repeat 3 times & record results
Identify magnetic degradation - compare
Notes: Pull testing
Clean the surface of the magnet
Select the appropriate test piece and spacers from the instruction manual (be consistent each time with the same equipment)
Zero the scale
Allow the piece to attract to the magnet (test in the center)
Pull the scale perpendicular to surface, slowly, smoothly, and evenly.
Repeat at least 3 times
Record the results.
Compare with previous results to identify any magnetic degradation