## Slide 1
Ethanol
Transportation and Storage
Hazards
Developed by Western Iowa Tech Community College
This material was produced under a grant (SH-16634-07-60-F-19) from the Occupational Safety and Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does the mention or trade names, commercial products, or organization imply endorsement by the U.S. government.
Notes: Transportation and storage concerns are a part of PSM

## Slide 2
Purpose
Create awareness of the hazards
Discuss the need for local emergency responder participation
Develop and practice an emergency plan for an accidental release

## Slide 3
There has been recent reports of an increase in accidental releases of ethanol into the environment.
Most are from train derailment and truck accidents that may be outside of the control of the plant managers.
Some of these are spills during transfers of ethanol or denaturant at the plants.
These are the ones we want to address!
Notes: One explanation for the recent increase in reported spills is the steep increase in ethanol production in the United States. A four-fold increase in production from 1999 to 2008, matched by a proportionate increase in the handling of denaturant by ethanol plants, means that the industry has had to hire and train many new employees.

## Slide 4
There is an estimated 250,000 ethanol transfer operations each year.
Even if these were performed with a 99.99 % success rate, there would be 25 spills each year.
Even a few high-profile spills involving fires or destruction of habitat will trigger a request for additional regulation and oversight.
Notes: A quick search through Internet reports suggests that the success rate is even better than 99.99 percent. The industry must be doing something right.

## Slide 5
Who is responsible for a leak when a rail tank car full of ethanol is shipped out from an ethanol production facility?
Is it the owner of the railcar?
No, the responsible party is the ethanol production facility that releases the tank car to the railroad for shipment.
Notes: Although rare, leaks from rail tank cars carrying hazardous substances do occur, and members of the ethanol industry need to be aware of potential liabilities.

## Slide 6
The ethanol industry produced 4 billion gallons in 2005, by 2012 that figure will nearly double.
As the ethanol industry continues to grow there is a need for producers to educate themselves on potential liabilities surrounding transportation of their product.
Notes: This is from an article from Ethanol Producer Magazine.

## Slide 7
Since rail transportation accounts for 75%of all the ethanol shipments, we will concentrate on that method.
Leaks from tank cars will happen;
  In a rail accident
  By mechanical failure
  Or by operator error
The first is usually unavoidable and relies on many external factors. The second and third have been termed “non-accident releases”, or NARs.
Notes: Trucking and barge shipments make up the other 25%. The hazards are going to be the same for all transportation.

## Slide 8
NARs consist of ;
  Leaks
  Splashes
  And other releases;
    Improperly secured or malfunctioning valves
    Fittings and tank shells
    Releases from pressure relief devices
The Association of American Railroads (AAR) created the North American NAR Reduction Task Force in 1995.
Notes: . By definition, a NAR is the unintentional release of a hazardous material while in transportation (including loading and unloading) and does not involve an accident. There are 1.7 million shipments of hazardous materials in the United States each year, and in 1996, the number of NARs topped 1,241 in the United States and Canada. In 2004, that number had been reduced to 673 NARs. However, the number climbed back to 716 in 2005. In general, the rail industry—and the top commodity shippers that use railcars to transport goods—are doing an admirable job in reducing NARs. However, with the tremendous growth in the ethanol industry, the potential for more alcohol-related NARs is something all producers need to prepare for in the coming months and years. In 2001, there were only 17 ethanol-related NARs, compared with an average of 42 per year from 2003 to 2005. Because ethanol is not shipped via pipeline, the transportation methods of choice are rail, truck and barge, with each segment hauling approximately 33 percent in 2004. In 2005, rail took over as the clear leader in ethanol transportation by hauling an estimated 75 percent of the total product, according to information presented at the American Coalition for Ethanol Conference & Trade Show conference in August. To keep up with the growing demand, the rail industry is building 4,000 to 5,000 rail tank cars every year specifically for shipping ethanol. In 2004, there were 68,960 carloads of ethanol shipped in North America, according to the latest report available from the Association of American Railroads Policy and Economics Department.

## Slide 9
The mission of the NAR Reduction Task Force is to reduce the number of NARs by
  Promoting proper “securement” of tank cars
  Their safe handling in transportation
  Increase awareness
  Encourage improved practices
  Gather data
  Distribute findings
Notes: The ultimate goal is to reduce NARs to zero.

## Slide 10
Between 2003 and 2005 the data team collected research from NARs in the ethanol industry.
It found that the manways and the bottom-outlet valves were the main sources for these leaks.
  In 20 instances, the manway bolts were loose
  In 5 instances, the gaskets were misaligned
  In 15 instances, the cap was loose while the valve was left open on the bottom-outlet
  And 10 incidents happened where the cap was loose and the valve was closed
Notes: The two big potential problem areas for NARs on a railcar are the manway and the bottom-outlet cap, Those are the two things that are open and closed on a daily basis.

## Slide 11
Follow Safe Loading and Unloading Methods as Outlined in Pamphlet 34
Reviewed and Changed by AAR
Notes: American Association of Railroads (AAR)

## Slide 12
Spills
Since alcohol and ethanol are polar solvents, their spills differ from gasoline and diesel.
Common FD Haz Mat booms and diking materials will not work with polar solvents, since the product damages the containment materials.
Most vacuum trucks will not work to recover ethanol, unless they have special filters designed for polar solvents.
Ethanol can be contained by diking with dirt or sand.
Spills should be prevented from entering sewers and waterways.
It may be necessary to cover the spill with alcohol resistant (AR) foam until the fuel can be recovered.
Merely letting the E-85 vapors evaporate does not solve the problem, because the gasoline will still remain.
Open flames should be kept away from the scene.
Clean-up can be very costly.
Notes: A discussion explaining the difference between a ethanol spill compared to gasoline or diesel.

## Slide 13
When should we get the local emergency responders involved?
If you wait until you need them , it could be too late!
Get them involved with your operations and have practice drills.
Notes: Ask the questions what will your role be in the event of a emergency or a spill?

## Slide 14
What steps do you need take if you an accidental release?
Do you report all releases? Just the large ones? How large?
How soon do you need to report a release?
Who do you report it to?
Notes: Topics for discussion will be by each training session.