## Slide 1: Fall Prevention Susan Harwood Training Grant Day 2

## Slide 2: Disclaimer
This material was produced under grant SH-19506-09-60-F-32 from the Occupational Safety and Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government.
Revisions were made to this material under grant number SH- 31240-SH7 from the Occupational Safety and Health Administration, U.S. Department of Labor.

## Slide 3: Test Review-1
Who is primarily responsible for providing employees with a fall protection system?
  The manufacturer of the fall protection system
  The employer
  The employee
  The insurer

## Slide 4: Test Review-2
You should report an accident immediately after it occurs so that____
  Someone else can use the machine
  First-aid can be applied if necessary
  Everyone else can see what's going on
  Your supervisor can hide the evidence

## Slide 5: Test Review-3
The ultimate responsibility for on-the-job safety rests with______
  You
  Your supervisor
  Human resources
  OSHA

## Slide 6: Test Review-4
The most common causes of injury on a construction site are _____
  Fires
  Choking
  Falls
  Faulty equipment

## Slide 7: Test Review-5
A floor hole wider than ______ must be protected.
  12 inches
  24 inches
  2 inches
  19 inches

## Slide 8: Test Review-6
A fall arrest system is required when a worker is operating at a height of ?
  3 feet or more
  6 feet or more
  10 feet or more
  None of the above

## Slide 9: Test Review-7
At what height do open‐sided floors in construction require guardrails?
  1 foot
  2 feet
  4 feet
  6 feet

## Slide 10: Test Review-8
An anchorage point for a Fall RESTRAINT system must be capable of supporting?
  5,000 pounds
  1,500 pounds
  12,000 pounds
  3,000 pounds

## Slide 11: Test Review-9
When fall arrest equipment is used, employers must assure that _________.
  All equipment is properly inspected before each use
  Users have calculated total fall distance
  A rescue plan is in place to rescue a fallen employee
  All of the above

## Slide 12: Test Review-10
What items and/or elements and/or approaches can be legally and safely used to help prevent falls during roof construction activities:
  Guardrails
  Covering holes and openings with sheathing
  Ensuring workers are properly and adequately trained
  All of the above

## Slide 13: Lesson Objectives
Fall prevention with scaffolding
Fall prevention with ladders
General review
Rescue planning
Post Test

## Slide 14: Scaffolding
An elevated, temporary work platform
3 types of scaffolds
  Supported scaffold : Rigid, load bearing parts, such as poles, legs, frames, and outriggers.
  Suspended scaffold: Suspended by ropes or other non-rigid overhead support.
  Aerial lifts such as “cherry pickers” or “boom trucks”

## Slide 15: Supported Scaffolding

## Slide 16: Supported Scaffolding Cont.

## Slide 17: Supported Scaffolding Example

## Slide 18: Scaffold Safety Hazards
https:www.youtube.com/watch?v=hJeUbaBdME0
Notes: Day 2-Slide 18: Fixed Scaffolds-Safety Hazards
Video: https://www.youtube.com/watch?v=hJeUbaBdME0

## Slide 19: Suspended Scaffolding

## Slide 20: Suspended Scaffolding Cont.

## Slide 21: Suspended Scaffold Example-Unsafe

## Slide 22: Suspended Scaffold Safe Example

## Slide 23: Aerial Lifts
Extendable boom platforms,
Aerial ladders,
Articulating (jointed) boom platforms,
Any combination of the above.

## Slide 24: Avoiding Risks
  Always follow manufacturer's instructions
  Install guardrail systems along all open sides and ends of platforms
  Personal fall arrest systems should be used on scaffolds higher than 10 feet
Notes:   Height of the scaffold should not be more than four times its minimum base dimension unless guys, ties, or braces are used.

## Slide 25: Avoiding Risks Weather
Do not work on snow or ice covered platforms during storms or high winds
Notes:   Height of the scaffold should not be more than four times its minimum base dimension unless guys, ties, or braces are used.

## Slide 26: Weather Risks
Warning: Video includes inappropriate language
https://www.youtube.com/watch?v=okS-hXB3jGg
Notes: Day 2-Slide26: Scaffolding Falling Off Building Downtown Portland, Oregon
Video: https://www.youtube.com/watch?v=okS-hXB3jGg

## Slide 27: Scaffolding Construction
Proper scaffold with a guard rail and a personal fall arrest system

## Slide 28: Scaffolding and Power Lines
Improper scaffold: Too close to the power lines

## Slide 29: Accidents Waiting To Happen
Inappropriate climbing on or off the scaffold
When working on unguarded scaffold platforms
Not checking platforms or planks for safety

## Slide 30: Dangerous Scaffolding!
Should be erected on an even and stable surface
Notes: The scaffold is not erected on an even base.

## Slide 31: Falling Objects
  Wear hardhats
  Barricade area below scaffold
  Use panels or screens if material is stacked higher than the toe board.
Notes: Toe board is the board used at the bottom side edge of the scaffold. If the material is stacked above it, there is a possibility that the materials will fall below and can hurt the workers worker below the scaffold.

## Slide 32: Platforms and Planks
  There are many requirements for construction of a scaffold to reduce your risk of falling
  Planks must be at least 18 inches wide
  Each plank end that abuts another must rest on a separate support surface
  Planks must be made of scaffold grade wood
Notes:   Planks must be at least 18 inches wide.
  Each abutted end of plank must rest on a separate support surface
  Overlap platforms at least 12 inches over supports, unless restrained to prevent movement.
  Only scaffold grade wood is to be used
  Each end of a platform, unless cleated or otherwise restrained by hooks, must extend over its support by at least 6 inches.

## Slide 33: Proper Access
Proper access
  Special ways to get on and off must be provided when scaffold platforms are more than 2 feet above or below a point of access.
  No access by cross braces
  Types of access permitted are:
    Ladders, such as portable, hook-on, attachable, stairway type, and built-ins
    Stair towers
    Ramps and walkways
Notes: 2 feet above or below a point of access made clear from the next slides

## Slide 34: Scaffolding Access
Bad
Better
Notes: Adequate, safe access must be provided when elevation changes more than 2 ft on scaffolds. Climbing cross braces is specifically disallowed, and can be very dangerous. The photo on the left shows wrong way of accessing the scaffolds. The photo on right shows the correct way of accessing the scaffold, when the they are above 2 ft above the access point

## Slide 35: What is wrong with this picture?

## Slide 36: Scaffolding and Fall Prevention Measures
No Sound Video https://www.youtube.com/watch?v=FyD5mpovxaw
Notes: Day 2-Slide 36: HAKI Universal Suspended Scaffold
Video: https://www.youtube.com/watch?v=FyD5mpovxaw

## Slide 37: Scaffolding and PFAS Demo
https://www.youtube.com/watch?v=w3Pb_FC9AfU
Video – no sound
Notes: Day 2-Slide 37: Energy absorbing fall arrest lanyard on scaffolding
Video: https://www.youtube.com/watch?v=w3Pb_FC9AfU

## Slide 38: Ladders
360 deaths every year
151,327 reported injuries per year caused by falls from ladders
Result of careless or improper ladder use
Follow safe practices to work safely

## Slide 39: Is it safe enough? Do’s!
Run this quick check on any ladder you are thinking of buying, or using:
  Is it sound? (clean, dry, free from wet paint, oil, mud, etc).
  Are there cracks?
  Are there rungs missing or loose?
  Is it painted?

## Slide 40: Is it safe enough? Don'ts!

## Slide 41: Are YOU up to the job?
Do not overestimate your physical abilities!

## Slide 42: Loads
Foldout and Leaning Ladders:
  Must be able to withstand 4 times the maximum intended load
Extra Heavy Duty or Plastic Ladders:
  Must be able to sustain 3.3 times the maximum intended load

## Slide 43: Ladder Labels

## Slide 44: Angles
Non Self Supporting Ladders
  Must lean against a wall or other support
  No more than ¼ of the working length of a horizontal distance at the base
Job Made Wooden Ladders
  Angle should equal about ½ of the working length

## Slide 45: Angle Demonstration
Day 2-Slide 45: Ladder Safety-How To Use An Extension Ladder Safely
Video: https://www.youtube.com/watch?v=GKNG_Ymf_dk
Notes: Day 2-Slide 45: Ladder Safety-How To Use An Extension Ladder Safely
Video: https://www.youtube.com/watch?v=GKNG_Ymf_dk

## Slide 46: Rungs, Cleats, or Steps
Must be parallel, level, and uniformly spaced
Rungs Spacing:
  Must be 10”-14” apart
  Trestle ladders must be 8”-18” for the base and 6”-12” inches on the extension
Rungs should be shaped so foot does not slide and be slip resistant

## Slide 47: Slipping
Kept free of oil, grease, wet paint, etc
Wood ladders must not be coated with opaque covering
  Except for warning labels on one side

## Slide 48: Other Requirements
Fold out or step ladders must have metal spreader or locking device
When using two or more ladders to reach a work area, they must be offset with a landing or platform between ladders
Area around top and bottom of ladders must be kept clear

## Slide 49: Portable Ladder Grades
There are 3 grades of portable ladders:
  Type 1 - Heavy-duty construction use
  Type 2 - Medium duty
  Type 3 - Home use, not for construction but contractors like to use them.

## Slide 50: Portable Ladder Type 1
Used for professional services: contractors, public utilities, and construction workers
Lengths of 3 to 20 feet
Has 3 subcategories:
  Type 1-Loads up to 250 lbs
  Type 1A-Loads up to 300 lbs
  Type 1AA-Loads up to 375 lbs
Heavy duty use

## Slide 51: Portable Ladder Type 2
Used for commercial services: painters, interior decorators, maintenance workers, electricians.
Lengths of 3 to 20 feet
Loads capacity to 225 lbs
Medium duty type use

## Slide 52: Portable Ladder Type 3
Used for household purposes
Lengths of 3 to 6 feet
Load capacity of 200 lbs
Light duty use

## Slide 53: Step Ladders
Self supporting, portable, A-frame

## Slide 54: Platform Ladders
Used for Special purposes
Has a large stable platform from which you can work while standing.

## Slide 55: Extension Ladder
Extension ladders are not self-supporting and are adjustable in length.

## Slide 56: Trestle Ladders
Self-supporting ladders that are not adjustable in length and have two hinged sections at the top so the legs form equal angles at the ladder’s base

## Slide 57: Going Up and Down Ladders
Face ladder at all times
Grasp side rails with both hands
Keep body between side rails
Never climb higher than 3rd rung from the top

## Slide 58: Going Up and Down Ladders Cont.
Raise and lower heavy, awkward loads with a hand line or hoist
Attach light, compact tools or materials to the ladder or to yourself
Use the 3 point rule

## Slide 59: Other Ladder Safety
Use nonconductive side rails such as wood or fiberglass when working near energized electrical lines
Avoid setting ladder near exit doors
Avoid using ladder near the path of pedestrian or vehicular traffic

## Slide 60: Ladder Don’t

## Slide 61: Ladder Don’t Cont.

## Slide 62: Ladder Don’t Ever

## Slide 63: No Safety, Know Pain
https://www.youtube.com/watch?v=Tbr_jjNUAfI
Notes: Slide 63: People Falling Off Ladders Compilation (Possibly Funny) - Not really
Video: https://www.youtube.com/watch?v=Tbr_jjNUAfI

## Slide 64: Fall Prevention Planning
Assess fall hazards in the work area
Fall protection applications employees will use
Correct procedures for use of PFAS
Correct procedures for handling, storage, and securing of tools and materials
Training methods for employees
Rescue plan
Plan must be jobsite specific
Fall protection plan must be available to all employees

## Slide 65: Fall Prevention Training
Employers shall provide training for each employee exposed to fall hazards
Each employee shall be trained by a competent person
  Nature of all fall hazards in the work area
  Correct procedures for erecting, maintaining, disassembling, and inspecting FPS
  Use of all fall protection systems
  Role of each employee when systems are being used

## Slide 66: Fall Rescue Planning
Addresses the procedures, equipment, and personnel needed to rescue when a fall occurs

## Slide 67: Suspension Trauma
Body weight causes pressure against harness
Reduces blood flow to heart
Worker can lose consciousness within minutes

## Slide 68: Rescue Techniques
Aided Rescue
Self-Rescue

## Slide 69: Aided Rescue
Suspended from a lifeline
Will need help from trained rescuers
May need medical attention

## Slide 70: Self Rescue
Worker can take steps to minimize trauma
Temporarily relieve pressure on legs
May attempt to lower themselves to lower level

## Slide 71: Self Rescue Demo
Show a self rescue video
Notes: Show a Harness Self Rescue after fall

## Slide 72: Communication Styles
  Aggressive: Dominating
  Passive: Submissive
  Assertive: Respectful

## Slide 73: Assertive Communication
Clearly states opinions and feelings
Values and respects themselves and others

## Slide 74: Assertive Communication Cont.
Don’t get angry; stay calm
Stick to the facts. (“That task is a fall risk.”)
State your position clearly without raising your voice
Seek compromise if possible

## Slide 75: Practice Assertiveness

## Slide 76: Fall Prevention Review
If you can fall more than 6 feet, you must be protected.
Use fall prevention on:
  Walkways & ramps, open sides & edges, holes, concrete forms & rebar, excavations, roofs, wall openings, bricklaying, residential construction
Protective measures include:
  Guardrails, covers, safety nets, and Personal Fall Arrest Systems

## Slide 77: Test Review-11
Inspections of scaffolds must be conducted?
  By a competent person
  Before each work shift
  After scaffold is erected or modified
  All of the above

## Slide 78: Test Review-12
If you are going to step onto a platform or roof, the top of the ladder should extend at least _____ feet above the point where the ladder touches the upper landing surface.
  2
  3
  4
  5

## Slide 79: Test Review-13
A type 1A ladder is rated for _____ use.
  200 pounds, light duty/household
  225 pounds, medium duty/commercial
  250 pounds, heavy duty/industrial
  300 pounds, extra heavy duty/professional

## Slide 80: Test Review-14
When should ladders be inspected?
  Each day before use
  At least once a week
  At least once a month
  At least once a year

## Slide 81: Post Test Time!

## Slide 82: Evaluation

## Slide 83: THANK YOU!