## Slide 1: Respirable Crystalline Silica in General Industry/Maritime Workplaces
Sample Employee Training Presentation
Developed by OSHA, 2019
NIOSH
Notes: Notes to employers and other trainers:
This is a sample presentation developed by OSHA to help employers or other instructors train employees covered under the OSHA respirable crystalline silica standard for general industry and maritime (29 CFR 1910.1053).
Employers and other instructors can customize this PowerPoint to meet their training needs. Examples of ways to customize this PowerPoint:
  Employers can add the specific tasks and controls used in their workplace.
  If exposures for a workplace do not trigger medical surveillance of any employees, extensive details about medical surveillance do not need to be discussed.
This presentation can either be projected or printed as handouts.
**Employees should be given a chance to ask questions about the material presented.**

## Slide 2: Respirable Crystalline Silica in General Industry/Maritime Workplaces
• This presentation contains copyrighted content. You may use, copy, distribute, and display the presentation as a whole. However, any copying, distribution, display, or modification of an individual copyrighted image or photo separate and apart from the presentation is not permitted without prior permission of the copyright holder, except as authorized by federal copyright law.
• The appearance of particular vendors or their equipment and/or services in this document does not constitute an endorsement by OSHA or the U.S. Department of Labor.

## Slide 3: What You Will Learn
What respirable crystalline silica is
How employees may be exposed
NIOSH
NIOSH
Notes: You are receiving this training because you may be exposed to respirable crystalline silica in your workplace.
This training will teach you:
  What respirable crystalline silica is; and
  The tasks done in your workplace that can expose you to respirable crystalline silica;

## Slide 4: What You Will Learn
              Workplace protections
              Silica Standard
Notes: This training will also teach you:
What employers must do to protect you, such as provide you with equipment that keeps dust out of the air. Such equipment could include a saw that applies water to the blade as it is cutting to prevent dust from getting into the air, as shown in the slide.
You will also learn about the major requirements that your employer must follow under the silica standard. “The silica standard” means the federal silica regulation that applies to general industry and maritime.

## Slide 5: What You Will Learn
Neil Lippy/Hoar Construction/elcosh.org
Amanda Mills/CDC
Health effects from breathing respirable crystalline silica
Medical surveillance
Amanda Mills/CDC
Notes: You will also learn how breathing in respirable crystalline silica can affect your health; and
The purpose of medical surveillance and what makes up a medical surveillance program. The medical surveillance requirements provide at-risk employees access to medical evaluations to help with early detection of health effects related to silica exposure.

## Slide 6: Crystalline Silica
NIOSH
Notes: We will start off by describing crystalline silica and how employees may be exposed.
Crystalline silica is a mineral. The most common form is quartz.

## Slide 7: Crystalline Silica Is Found In Many Common Materials
John F. Rekus, PE, MS, CIH, FAIHA/elcosh.org
NIOSH
Notes: Crystalline silica is found in many materials used in general industry and maritime workplaces:
This includes natural materials such as stone and sand.
It also includes man-made materials such as artificial stone.

## Slide 8: Respirable Crystalline Silica
NIOSH
NIOSH
American Foundry Society
Notes: Exposures to respirable crystalline silica can occur, for example, during the manufacturing of products such as glass, pottery, ceramics, brick, concrete, and artificial stone. Other examples of exposures include during abrasive blasting with sand, and during the use of industrial sand in operations such as foundry work and hydraulic fracturing. The picture on the left shows a worker grinding a sand-based casting in a foundry.
Respirable crystalline silica particles are very small -- about 100 times smaller than a grain of sand found on the beach. In the picture on the right, the pen is pointing to grains of sand that are similar in size to sand found on the beach. To the right of that sand is dust made up mostly of respirable crystalline silica. The picture shows how much finer respirable crystalline silica is than beach sand.
When these very fine respirable silica particles are breathed in, they can travel deep into the lungs, where they can become trapped and cause disease.
(For the remainder of this training, we will simply refer to “silica,” when we talk about respirable crystalline silica.)

## Slide 9: Workplace Tasks with Exposure
Employers must train employees on tasks in their workplace that may expose them to respirable crystalline silica
Notes: Note to employers: Employers must train employees on the specific tasks that could expose employees to silica in their workplace (for example, during cutting or grinding of granite countertops). This slide can be modified to include those specific tasks.

## Slide 10: Health Hazards of Silica
Silicosis
Lung cancer
Chronic obstructive pulmonary disease (COPD)
Kidney diseases
Autoimmune diseases
Notes: Breathing in silica can increase employees’ chances of developing lung diseases, including silicosis, lung cancer, and chronic obstructive pulmonary disease (COPD). It also increases their chances of developing kidney and autoimmune diseases.
The higher the levels of silica that employees are exposed to and the longer they are exposed to it, the greater the chances of developing these diseases.
Silicosis and COPD are lung diseases that are permanent and not curable, and can become deadly or disabling.
Less than 16 percent of people diagnosed with lung cancer live longer than five years.
Kidney diseases can cause problems like high blood pressure or even end-stage renal disease, which often requires dialysis or a kidney transplant.
Autoimmune diseases occur when antibodies that protect the body from diseases attack the body itself.
  Rheumatoid arthritis is an example of an autoimmune disease.

## Slide 11: Health Hazards - Silicosis
Three types:
  Chronic
  Accelerated
  Acute
Permanent
Can be debilitating or deadly
Healthy Lung
Silicotic Lung
CDC
CDC
Notes: Employees exposed to silica could develop silicosis.
There are three forms of silicosis that can develop, based on how much silica employees are exposed to and for how long.
  Most employees who develop silicosis develop chronic silicosis. It typically develops after repeated exposures over 10 or more years.
  Accelerated silicosis typically develops after 5-10 years of exposure to higher levels.
  Acute silicosis typically develops after exposures to extremely high levels, such as could occur with abrasive blasting with sand. It usually occurs within a few months to less than two years of exposure. It is the rarest form of silicosis.
All forms of silicosis are permanent and irreversible. This means that once you have silicosis, it does not go away or get better and there is no way to cure it. Silicosis can get worse over time and can lead to disability or death.
The top picture shows a healthy lung and the bottom picture shows a lung from a silicosis victim.

## Slide 12: Symptoms of Lung Diseases
Sometimes, no symptoms in early stage of disease
Coughing and shortness of breath
Fever, weight loss, exhaustion, and coughing up blood
Notes: Employees might not have symptoms in the early stages of silica-related diseases, but symptoms can develop as the diseases get worse over time.
Symptoms of lung diseases associated with silica exposure include shortness of breath and coughing. In some employees, these symptoms can get so severe that they cannot work or do common, everyday activities. For example, someone with silicosis might have trouble walking at a normal speed or going up stairs.
Fever, weight loss, exhaustion, and coughing up blood can occur with severe lung disease, lung cancer, and lung infections.
People who have lung diseases, such as silicosis, have a greater chance of developing lung infections such as the flu and pneumonia.

## Slide 13: Protecting Employees
Hierarchy of Controls
Notes: Your employer must protect you from being exposed to silica dust above certain levels. This decreases the chances that you will develop silica-related diseases.
This pyramid shows OSHA’s hierarchy of controls, which lists the types of controls in order of their effectiveness.
It shows the most effective form of protection – engineering controls – at the top of the pyramid. Engineering controls remove or isolate silica dust at the point where it is made.
The second-most effective type of protection is work practice controls. Work practice controls involve doing tasks in ways that reduce dust exposure.
The least effective type of protection is personal protective equipment, such as respirators. This is shown at the bottom of the pyramid.
The silica standard requires employers to use engineering controls and work practice controls first to reduce exposures. They can have employees use respirators only if engineering and work practice controls aren’t sufficient to reduce exposures.

## Slide 14: Engineering Controls
Department of Labor/Shawn T Moore
No engineering controls
Using water to control dust
Cutting stone
California Department of Public Health
California Department of Public Health
Notes: The three major types of engineering controls for silica dust are wet methods, vacuum dust collection systems, and isolation.
Wet methods involve using water or a foam to keep dust down and out of the air.
These pictures show cutting stone, with and without the use of water.
The picture on the right shows how water greatly reduces the dust released into the air.

## Slide 15: Engineering Controls
Department of Labor/Shawn T Moore
Grinding Stone
Using a vacuum dust
collection system
No engineering controls
NIOSH
Notes: Another type of engineering control for silica dust is a vacuum dust collection system.
Vacuum dust collection systems remove dust at the point where it is made.
These pictures show employees grinding stone, with and without a dust collection system.
The pictures show how capturing the dust at the point where it is made greatly reduces the amount of dust in the air.

## Slide 16: Engineering Controls
Employee protected by enclosure that isolates dust during abrasive blasting of dental castings
New Jersey Department of Health
Notes: The third type of engineering control used for silica dust is isolation.
Isolation separates the employee from silica dust.
This photo shows an enclosure that protects the employee from dust created during abrasive blasting of dental castings

## Slide 17: Engineering Controls for Hydraulic Fracturing
Required by June 23, 2021
NIOSH
Notes: Note that if you are exposed to silica dust from hydraulic fracturing operations in the oil and gas industry, your employer has until June 23, 2021, to control silica exposures using engineering controls.
Currently, hydraulic fracturing employers must follow all other requirements of the standard, such as using respirators to protect employees from exposures above the PEL.
This picture shows mini bag houses that prevent the release of silica dust during sand transfer operations at hydraulic fracturing sites.
[Note to employers and other trainers: This slide can be deleted if you are training workers who are not involved with hydraulic fracturing in the oil and gas industry]

## Slide 18: Work Practice Controls
Example: Fixing controls that are not working properly
Department of Labor/Shawn T Moore
Notes: Training on how to use effective work practices is another way employers can protect their employees.
Work practice controls involve doing tasks in ways that decrease exposures.
One type of a work practice control is making sure that engineering controls are working properly. An example is checking that vacuum systems are functioning effectively and not releasing dust.
Immediately addressing an engineering control that is not working properly is another example of a work practice control. If you can see dust levels starting to increase, as is shown in this picture, this is a sign of a problem with engineering controls.
Another example of a work practice control is using cleaning methods, such as wet sweeping, to decrease the amount of dust that gets into the air.
Your employer might also schedule dusty tasks when other employees will not be around.

## Slide 19: Respirators
Department of Labor/Shawn T Moore
Notes: Personal protective equipment, such as respirators, is at the bottom of the hierarchy of controls.
Your employer must give you a respirator if engineering controls and work practices are not enough to control exposures down to the exposure limit.
Even when respirators must be used, your employer must still use engineering and work practice controls to lower exposures as much as possible.
One of the major reasons why engineering and work practice controls must always be used before respirators is because they decrease dust at the point where it is made. As a result, they protect everyone in the area.
Respirators are effective if they are properly selected, fitted, maintained, and worn. However, they protect only the people wearing them.

## Slide 20: Specific Protections in This Workplace
Employers must train employees on workplace-specific:
Engineering controls
Work practice controls
Respiratory protection
Notes: Note 1 to employers: Employers must inform employees of the specific engineering controls, work practice controls, and respiratory protection used in their workplace. If exposures are controlled by substituting a different material for a silica-containing material, employees must be trained on that as well. The controls used in the workplace can be included as part of this slide if it is convenient for employers.
Note 2 to employers: Employees must be trained on the proper work practices associated with the tasks they perform. For example, an employee who operates equipment with built-in dust controls must know how to fully and properly implement and maintain the dust controls on that equipment.
Note to trainers other than employers: The slide can be modified to let employees know that their employers must train them about the specific engineering controls, work practices, and respiratory protection used in their workplace. They should also know that the employer should show them how to fully and properly implement controls for any tools they operate.

## Slide 21: Respirable Crystalline Silica Standard for General Industry and Maritime
Notes: We will now talk about the major requirements of the silica standard for general industry.

## Slide 22: Permissible Exposure Limit (PEL)
50 Micrograms per Cubic Meter of Air (µg/m3)
Averaged over an 8-hour work day
Notes: Employers must determine how much silica you are exposed to and whether your exposure is at or below the permissible exposure limit (PEL). The PEL is 50 micrograms of respirable crystalline silica per cubic meter of air averaged over an 8-hour work day (µg/m3).
The units of µg/m3 represent the weight of respirable crystalline silica suspended in a specific amount of air.

## Slide 23: Perspective on PEL
1,000 µg in the air of this room = 50 µg/m3
2.4 meters
3.1 meters
2.7 meters
1,000 µg of silica
20 cubic meters of air
Notes: The photo on the left shows 1,000 micrograms of respirable crystalline silica next to a dime.
The photo on the right shows a room that contains approximately 20 cubic meters of air.
1,000 micrograms of respirable crystalline silica suspended in 20 cubic meters of air is an average concentration of 50 micrograms per cubic meter, which is equal to the PEL.
A person who worked in this room for no more than 8 hours would not be exposed to silica above the PEL.
You might not notice 1,000 micrograms of pure respirable crystalline silica dust when it’s airborne in a room of this size. But, because silica is typically a small part of total dust, the air would likely be noticeably dusty.
Your exposures to silica may increase and decrease throughout the shift.
For example, you may be exposed while performing a silica-generating task and then not receive additional exposures when performing a task that doesn’t generate silica dust.
Although exposures are increasing and decreasing throughout the shift, your average exposure must remain at or below 50 µg/m3 for each 8-hour work shift.

## Slide 24: Exposure Assessment
Employers must:
Determine exposures
Give employees results
Let representatives observe
Construction Safety Council
Notes: Your employer must determine how much respirable crystalline silica you are exposed to.
Employers can determine exposure to silica in different ways.
  They might measure exposures by attaching a pump to you that collects silica dust. This picture shows the pump attached to an employee’s belt. The pump draws in air through the cyclone, which is the device attached near the employee’s collar. The cyclone contains a filter that is sent to the lab to determine the employee’s exposure level.
  Employers might also determine exposures using other methods. For example, some meters directly measure the concentration of total respirable dust. The amount of silica can then be determined based on the fraction of silica in the material being worked on or used in the production process, such as sand, stone, or artificial stone.
  (Note: Under the hazard communication standard, employers must train employees on how silica is detected in the workplace.)
Employers must notify you about your exposure levels within 15 days of getting the results. They can notify you personally or by posting the results in a convenient location (employers should let employees know how they will be notified).
Employers must also notify you about corrective actions they will be taking if exposures exceed the PEL. Corrective actions might include use of engineering controls and/or respirators.
Employers must also let you or your representative observe exposure measurements that they take in the workplace.

## Slide 25: Methods of Compliance
Employers must select:
Engineering controls
Work practice controls
Respirators, if needed
Hierarchy of Controls
Notes: Your employer must follow OSHA’s hierarchy of controls to determine effective engineering and work practice controls and must require the use of respirators only when those controls are not enough to decrease exposures to the PEL or below.
Even if employers cannot reduce exposures to the PEL with engineering and work practice controls, they must reduce exposures as much as possible using those controls.

## Slide 26: Respiratory Protection
Employers must:
Provide respirators if needed
Follow the respiratory protection standard
Department of Labor/Shawn T Moore
Notes: As mentioned earlier in the presentation, in some cases employers must provide you with respirators to protect you from breathing in silica dust.
If respirators are used in the workplace, employers must follow all requirements of the respiratory protection standard, including training about respirators, testing to make sure respirators fit properly, and providing medical evaluations.

## Slide 27: Regulated Areas
Establish where exposures are expected to exceed PEL
Mark off the area
Post warning signs at entrances
Limit access
Provide and require use of respirators
Photo by Samuel Zeller on Unsplash
Notes: Employers must establish regulated areas wherever exposures to silica are expected to be greater than the PEL.
The purpose of regulated areas is to let employees know about designated high-exposure areas, limit the numbers of employees in those areas, and ensure that whoever enters those areas wears a respirator.
Employers must mark off regulated areas in some manner, such as by using cones, tape, barricades, or textured flooring.
Warning signs with specific wording must be posted at all entrances to regulated areas.
Only authorized persons are allowed to enter regulated areas. This includes persons who must work in the area, such as employees who repair or maintain equipment in the areas, and quality control staff who must enter those areas to do their job.
Employers must provide an appropriate respirator to those who enter the area; they must make sure that everyone who enters the area uses the respirator the entire time he or she is in the area.

## Slide 28: Regulated Area – Warning Sign
RESPIRABLE CRYSTALLINE SILICA
MAY CAUSE CANCER
CAUSES DAMAGE TO LUNGS
WEAR RESPIRATORY PROTECTION IN THIS AREA
AUTHORIZED PERSONNEL ONLY
DANGER
Notes: Warning signs at each entrance of a regulated area must have this wording.

## Slide 29: Housekeeping
When cleaning silica dust, avoid:
Dry sweeping/brushing
Compressed air without a ventilation system to capture the dust
Mount Sinai/CHEP/elcosh.org
Notes: Certain cleaning methods can increase employee exposures to silica by releasing dust into the air.
Therefore, the silica standard requires employers to avoid cleaning methods that release dust into the air; and to use cleaning methods that reduce the likelihood of exposures.
Dry sweeping and dry brushing should not be used if they can contribute to silica exposures.
Compressed air should not be used to clean clothing or surfaces, unless the compressed air is used with a ventilation system that captures and gets rid of the dust in a way that prevents workers from being exposed.
Less dusty cleaning methods, such as HEPA-filtered vacuuming, wet sweeping, or the use of oil- or wax-based sweeping compounds, should be used instead.
  Employers can, however, use dry sweeping, dry brushing, or compressed air when the less dusty cleaning methods would cause damage, create a hazard in the workplace, or be ineffective. Examples of housekeeping methods that would create a hazard include wet sweeping near electrical equipment, or using water near molten metal, which can result in an explosion.
Note: A HEPA-filtered vacuum is a type of vacuum that effectively captures respirable dust.
Note: The housekeeping prohibitions in the standard do not apply when cleaning up materials that can’t release respirable crystalline silica, such as ordinary dirt, beach sand, large debris, or saw dust.

## Slide 30: Housekeeping
Employers must let employees know which housekeeping methods:
  Must be used in the workplace
  Must not be used in the workplace
Notes: Note to employers: Because proper housekeeping is a work practice that controls exposures, employers must train employees on the specific housekeeping methods used in their workplace. Employers can update this slide to address the cleaning practices that should be used and practices that must not be used in their workplace.

## Slide 31: Written Exposure Control Plan
Employers must:
Prepare and implement it
Review it yearly
Make it available
Written Exposure Control Plan
Tasks with Exposure:
Engineering/Work Practice Controls:
Respiratory Protection:
Housekeeping:
Notes: Employers must prepare and implement a written exposure control plan.
The plan must:
  Describe tasks involving exposure to silica;
  Describe the engineering controls, work practices, and respiratory protection used for each task; and
  Describe housekeeping measures used to limit worker exposure to silica.
Your employer must review the plan at least once a year and make any updates if needed.
Your employer must let you and your representative look at or copy the written exposure control plan if requested.
(Employers should let employees know where they can view or request a copy of the written exposure control plan).

## Slide 32: Medical Surveillance
For employees exposed to silica for 30 or more days/year:
  Above the PEL (until June 23, 2020)
  At or above the action level (starting June 23, 2020)
Amanda Mills/CDC
Offered:
  Within 30 days of assignment
  Every three years
Notes: From now until June 23, 2020, employers must offer you a medical exam if you will be exposed to silica above the PEL for 30 or more days a year.
Beginning on June 23, 2020, employers must offer you a medical exam if you will be exposed to silica at or above the action level, which is 25 µg/m3, averaged over an 8-hour work day, for 30 or more days a year.
The employer must offer you an initial medical exam within 30 days of assigning you to a job that will result in you meeting the trigger for medical surveillance, unless you have had a medical exam for silica within the last three years.
The employer must continue to offer periodic medical exams at least every three years if you will meet the trigger for medical surveillance.
Note that the medical exam for silica is different than the medical evaluation required by the respiratory protection standard. If you will be required to wear a respirator, you must undergo the medical evaluation for respiratory protection before you are fit tested for the respirator or wear the respirator in the workplace.

## Slide 33: Medical Exams
Medical and work history
Physical exam
X-rays
Lauren Bishop/CDC
Notes: If you have a medical exam, it will include:
  A medical and work history. This will include questions about your health, past jobs you have done, and the exposures in those jobs;
  A physical exam, including listening to your heart and lungs with a stethoscope, and measuring blood pressure; and
  A chest X-ray to help evaluate the health of your lungs.

## Slide 34: Medical Exams
Lung function test
Tuberculosis (TB test)
CDC
Vitalograph, http://vitalograph.com/imagelibrary
Notes: The medical exam also includes:
A lung function test. This involves using an instrument called a spirometer to measure how much air you can blow out and how fast you can blow it out after taking a deep breath, as shown in this picture.
A tuberculosis (TB) test. A TB test is done only for the initial exam, which is the first exam that you receive under the silica standard.
  The purpose of the test is to determine if you have a latent TB infection. Latent TB is a stage of TB infection in which a person does not have signs or symptoms of TB and cannot spread the disease to others. Latent TB cannot be detected with a chest X-ray, so a skin test is needed.
  Testing for TB is done because exposure to silica can increase the chances that someone with a latent TB infection can develop active TB disease. A person with active TB disease has symptoms and can spread the disease to others.
  If you were born or grew up in a country other than the U.S., you should let the health care professional know. Many countries outside the U.S. vaccinate children to prevent TB-related diseases. Persons who have received the vaccine and are given the skin test for TB may have a false positive finding. This means that they appear to have a latent TB infection, when they are not actually infected. If you grew up in a country that vaccinates children for TB diseases, the health care professional might consider a blood test instead of a skin test for TB. This would decrease the chances of a false positive finding.

## Slide 35: Why Medical Exams are Important
Find disease or increased sensitivity to silica exposure
Determine fitness to use respirator
Department of Labor/Shawn T Moore
Notes: Getting the exam is important for the following reasons:
  First, an exam can determine whether you have a disease related to silica exposure. This will allow you to take actions to protect your health, including: quitting smoking; getting jobs with lower exposures to silica; or getting flu shots.
  The exam will also determine whether you might have any condition, such as a lung disease, that is not caused by silica exposure but that might make you more sensitive to silica exposure.
  In addition, the exam will let you know whether you have a health condition that does not allow you to wear certain kinds of respirators. This could prevent you from endangering your health or life by wearing the wrong kind of respirator.

## Slide 36: Medical Report for the Employee
Medical conditions
Recommended limitations on respirator use and exposure to silica
Recommendation for specialist exam
Only goes to the employee
Notes: If you have had a medical exam, your employer must make sure that the healthcare professional explains the results of the medical exam to you and gives you a written medical report within 30 days of the exam.
The report must include the following information:
  If you have a medical condition related to silica exposure or one that might make you more sensitive to silica exposure;
  If the healthcare professional recommends limiting exposure to silica;
  If the health care professional recommends that you be examined by a specialist.
The healthcare professional does not give a copy of the report to your employer; it belongs to you alone.

## Slide 37: Medical Opinion for the Employer
Additional information requiring employee consent:
  Recommended exposure limitations
  Recommendation for specialist exam
Only medical info included:
  Recommended respirator limitations
Photo by rawpixel.com on Unsplash
Notes: The employer will get a written medical opinion from the healthcare professional.
The opinion that your employer gets is different than the report you get.
The written opinion to your employer will include the exam date, a statement that the exam met the requirements of the silica standard, and any recommended limitations on respirator use.
Only if you give written permission to the healthcare provider will the medical opinion for your employer include more information. This could include recommended limitations on silica exposure, or a recommendation for a specialist exam. You can authorize either one or both recommendations to be included in the opinion to the employer.
Your employer does not receive information about your health because employees might fear retaliation or discrimination based on this information.
Under the Occupational Safety and Health Act, employers must not discriminate or retaliate against employees for participating in medical surveillance or based on the results of their medical exam.

## Slide 38: Written Medical Opinion
Employees also get a copy
Proof of exam for future employers
Notes: You must receive a copy of the written medical opinion that went to your employer within 30 days of the exam.
You should hold onto that opinion because you can use it as proof of a current medical exam for future employers.
This will prevent you from getting medical tests more often than required.

## Slide 39: Exams at No Cost to Employees
Employer covers costs of:
Exams
Tests
Time spent traveling and getting exam
Notes: Employers must offer exams at a reasonable time and place and cover all costs of medical exams. This includes:
  Cost of the exam;
  Costs of tests – including additional tests that are related to silica exposure; and
  Costs of specialist exams.
If you get a medical exam, your employer must also cover the costs of travel and pay you for the
  Time spent getting the exam
  Time spent traveling to and from the exam.
Your employer must pay for an additional medical exam by a specialist, but only if you authorize your employer to receive the recommendation for the specialist exam.
The healthcare professional might let you know about other health conditions that are not related to silica exposures. Employers are not responsible for costs of additional exams or tests for conditions that are not related to silica. You will need to see your personal health care provider about those conditions.

## Slide 40: Other Training
Hazard communication program
Respiratory protection program
United Steelworkers – Tony Mazzocchi Center
Notes: Employees exposed to silica in their workplace must also receive training under other OSHA standards.
The hazard communication standard requires that you be trained on the written hazard communication program in your workplace and where to find information about those hazards. The hazard communication standard also requires that employees be trained on how substances such as silica are detected in the workplace.
If respirators are used in your workplace, you must also receive the training required under the respiratory protection standard.

## Slide 41: Copy of the Standard
Employers must:
Make a copy of the standard available to employees at no charge
Notes: Employers must make a copy of the standard available to you and let you know how you can view it, free of charge.
Employers can update this slide to include this information.
Note to employers: This slide can be updated to include information on how employees can get access to a copy of the standard.

## Slide 42: Recordkeeping
Employers must:
Keep medical and exposure records
Make them available
Photo by Andrew Pons on Unsplash
Notes: Employers must keep exposure and medical records.
If you or your representative requests these records, employers must make them available.

## Slide 43: More Information
www.osha.gov/silica/